3GPP TSG-SA5 Meeting #154 	S5-242021d3

Changsha, China, 15 - 19 April 2024

# Source:	ZTE Corporation

# Title:	pCR TR 28.915 Use case on network failure and risk prediction

# Document for:	Approval

Agenda Item:	6.19.5

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

- ETSI GR ZSM-15: "Zero Touch Network and Service Management (ZSM); Network Digital Twin".

- 3GPP TR 28.915: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Study on management aspects of Network Digital Twin (Release 19) "

# 3	Rationale

Network Digital Twins are an increasingly examined technology relevant to system automation. A NDT is a virtual replica of a real-world system on which operations can be performed for simulation and verification of physical network and services. The observed outcomes and effects of such operations constitute information that can be used to inform operational decision-making.

A network digital twin can be used to simulate part or all of RAN and 5GC physical network including network slice instance, network slice subnet instance and NFs in high fidelity, various of possible failures and risks which may be happened in the future in physical network can be accurately predicted by network digital twin, we can pre-adjust network optimization policies to avoid their occurrence based on the results of prediction.

# 4	Detailed proposal

1st Change

# 5	Use cases

## 5.X Use case#x: Network failure and risk prediction

### 5.X.1 Description

Each operations for network optimization and maintenance on mobile network may cause potential network failures and risks, especially high-risk operations, such as potentially dangerous configuration modification, policy modification, software version upgrade, and board switching, which may cause network congestion and network breakdown. To avoid any impact on the physical network, we can’t carry out the potential high-risk network operations in the physical network directly without concerning any consequences, and we can’t use the physical network to evaluate possible network optimization strategy and solution directly. Therefore, it is the better way that these network operations and possible network optimization solutions can be simulated and evaluated using network digital twin.

3GPP network system can decide using the NDT to handle potential high-risk operations. Using NDT, high-risk operations can  identify whether these operations may cause potential network failures and risks by performing necessary digital twin related operations, e.g. simulation, verification and evaluation. The NDT can also optimize, verify and evaluate possible network policies and solutions for the further risk avoidance. After simulating and evaluating by the NDT,  the results of high-risk operations prediction and evaluation should be notified back to 3GPP network system.

In addition, SLA degradation and failure of single node in mobile network can also be predicted using the NDT. When it is predicted that the network resources in the network domain are not enough to maintain the SLA or hardware resources failure at some time in the future, the NDT should warn 3GPP management system to take actions for network failure and risk avoidance.

Another scenario of network slice risk prediction is described in clause 5.2[1]. Using the NDT to predict risks, the ZSM framework can identify risks of specific service or network slice profile parameters not being met due to changing traffic and network conditions (e.g. a MD not being able to provide the network slice latency it committed for) and the NDT supports the ZSM framework to take actions before these risks materialize and therefore before the committed SLA/SLS are broken.

Therefore, 3GPP network system has needs to use network digital twin to predict and evaluate potential network failures and risks based on operator’s requirements, such as predict possible network failures and risks posed by the high-risk operation. 3GPP management system can also use the NDT to evaluate and verify possible network policies and solutions to minimize the impact of high-risk operations.

### 5.X.2 Potential requirements

REQ-NDTN_Failurerisk-1:  The NDT should have the capability allowing the consumer  to request evaluation of the risk level for high-risk operations.

Note: High-risk operations may be proposed changes to the network configuration, proposed updates to the network policies, etc.

REQ-NDTN_ Failurerisk-2: The NDT should have the capability to provide the results of evaluation of risk level for high-risk operations.

REQ-NDTN_ Failurerisk-3:  The NDT should have the capability allowing the consumer to request to evaluate and verify possible network policies and solutions which minimize the risk level of high-risk operations.

### 5.X.3 Potential solutions

### 5.X.4 Evaluation of potential solutions

End of changes