3GPP TSG-SA5 Meeting #154 	S5-242043d1

Changsha, China, 15 - 19 April 2024

# Source:	Huawei

# Title:	Rel-19 pCR 28.866 Add use case for fault analytics time duration measurement

# Document for:	Approval

Agenda Item:	6.19.2

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

[1] 	3GPP TR 28.866: “Study on Management Data Analytics (MDA) – Phase 3”.

# 3	Rationale

This contribution proposes the new use case on the topic of fault management related analytics for TR 28.866 [1]. This is related to WT-7 in the SID.

MDA has the capability for failure prediction and service failure recovery as defined in TS 28.104. It may be useful to evaluate the capability for MDA to perform fault analytics. It can be achieved by measuring the time duration of fault analytics with a specific type. Currently, there is no clear statement on the measurement method of the time duration of fault analytics.

# 4	Detailed proposal

It is proposed to make the following changes to TR 28.866 [1].

1st change

## 5.X		Use case X: Fault analytics time duration measurement

### 5.X.1		Description

In MDA assisted fault management, consumers can obtain analytics output which includes predictions of potential service failures and possible recommendation actions to prevent failures or service recovery. It is beneficial to evaluate the capability for MDA to perform fault analytics by measuring the time duration of fault analytics with a specific type. It may help consumer decide when to request the analytics or evaluate the timeliness of obtaining fault analytics results. For example, it is useful for consumer to measure the time duration of failure prediction assisted by MDA in order to evaluate the speed of failure prediction and timeliness of subsequent failure prevention actions.

In TS 28.104 [x], MDAOutputs contains an attribute analyticsWindow which indicates the time duration related to an MDA output. In order to measure the time duration fault analytics with a specific type, there needs clear statement on the measurement method, such as adding reasonable description or additional attributes in the analytics output.

### 5.X.2		Potential Requirements

REQ-MDA-01: The MDA capability for fault management related analytics may be able to enable MnS consumer to obtain the analytics output including the measurement of time duration of fault analytics with a specific type from MDAS producer.

### 5.X.3		Potential Solutions

TBD

End of changes