.3GPP TSG-SA5 Meeting #154 	S5-242081

Changsha, China, 15 - 19 April 2024

# Source:	Ericsson

# Title:	pCR 28.871-000 Inventory of 5G NRM specifications

# Document for:	Approval

Agenda Item:	6.19.8

# 1	Decision/action requested

Approve the pCR.

# 2	References

[1]	3GPP TS 28.871 Study on Service Based Management Architecture enhancement phase 3

[2]		28.622 Telecommunication management; Generic Network Resource Model (NRM) Integration Reference Point (IRP); Information Service (IS)

[3]	28.541 Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3

[4]	28.104 Management and orchestration; Management Data Analytics (MDA)

[5]	28.105 Management and orchestration; Artificial Intelligence/ Machine Learning (AI/ML) management

[6]	28.111 Fault management

[7]	28.311 Management and orchestration; Network policy management for mobile networks based on Network Function Virtualization (NFV) scenarios

[8]	28.312 Management and orchestration; Intent driven management services for mobile networks

[9]	28.317 Management and orchestration; Self-configuration of Rad io Access Network Entities (RAN NEs)

[10]	28.318 Management and Orchestration; Network and services operations for energy utilities

[11]	28.319 Management and orchestration; Access Control for Management services

[12]	28.532 Management and orchestration; Generic management services

[13]	28.536 Management and orchestration; Management services for communication service assurance; Stage 2 and stage 3

[14]	28.538 Management and orchestration; Edge Computing Management

[15]	28.556 Management and orchestration; Network policy management for 5G mobile networks; Stage 2 and stage 3

# 3	Rationale

One important argument when introducing SBMA was to get away from the fragmented specification structure that IRP architecture has.

The NRM fragments are spread over many TSs. For an implementer it is difficult to know which specifications are applicable to the design that is to be made. Especially as many of the TSs do not even have NRM in the title.
Furthermore, there is no information on dependences of the NRM TSs that depend on another NRM TS(s).

# 4	Detailed proposal

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

…

[x]	<doctype> <#>[ ([up to and including]{yyyy[-mm]|V<a[.b[.c]]>}[onwards])]: "<Title>".

[a]		28.622 Telecommunication management; Generic Network Resource Model (NRM) Integration Reference Point (IRP); Information Service (IS)

[b]	28.541 Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3

[c]	28.104 Management and orchestration; Management Data Analytics (MDA)

[d]	28.105 Management and orchestration; Artificial Intelligence/ Machine Learning (AI/ML) management

[e]	28.111 Fault management

[f]	28.311 Management and orchestration; Network policy management for mobile networks based on Network Function Virtualization (NFV) scenarios

[g]	28.312 Management and orchestration; Intent driven management services for mobile networks

[h]	28.317 Management and orchestration; Self-configuration of Rad io Access Network Entities (RAN NEs)

[i]	28.318 Management and Orchestration; Network and services operations for energy utilities

[j]	28.319 Management and orchestration; Access Control for Management services

[k]	28.532 Management and orchestration; Generic management services

[l]	28.536 Management and orchestration; Management services for communication service assurance; Stage 2 and stage 3

[m]	28.538 Management and orchestration; Edge Computing Management

[n]	28.556 Management and orchestration; Network policy management for 5G mobile networks; Stage 2 and stage 3

## 5.X	NRM investigation

### 5.x.1	Description

One important argument when introducing SBMA was to get away from the fragmented specification structure that IRP architecture has.

The following TSs contain stage 2 NRM fragments specified for 5G:

28.622 Telecommunication management; Generic Network Resource Model (NRM) Integration Reference Point (IRP); Information Service (IS) [a]

28.541 Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3 [b]

28.104 Management and orchestration; Management Data Analytics (MDA) [c]

28.105 Management and orchestration; Artificial Intelligence/ Machine Learning (AI/ML) management [d]

28.111 Fault management [e]

28.311 Management and orchestration; Network policy management for mobile networks based on Network Function Virtualization (NFV) scenarios [f]

28.312 Management and orchestration; Intent driven management services for mobile networks [g]

28.317 Management and orchestration; Self-configuration of Radio Access Network Entities (RAN NEs) [h]

28.318 Management and Orchestration; Network and services operations for energy utilities [i]

28.319 Management and orchestration; Access Control for Management services [j]

28.532 Management and orchestration; Generic management services [k]

28.536 Management and orchestration; Management services for communication service assurance; Stage 2 and stage 3 [l]

28.538 Management and orchestration; Edge Computing Management [m]

28.556 Management and orchestration; Network policy management for 5G mobile networks; Stage 2 and stage 3 [n]

# 5.x.2 Potential requirement

NA.