3GPP TSG-SA5 Meeting #154 	S5-242093

Changsha, China, 15 - 19 April 2024

# Source:	Ericsson

# Title:	pCR TR 28.873 Add introduction for data management regarding subscriptions and reporting

# Document for:	Approval

Agenda Item:	6.19.11

# 1	Decision/action requested

The group is asked to approve the proposal.

# 2	References

[1]	TR 28.873 " Study on data management, subscriptions and reporting"

[2]	SP-231732 "Study on data management regarding subscriptions and reporting"

# 3	Rationale

This contribution proposes to add introduction for TR 28.873 [1] based on SP-231732 [2]

# 4	Detailed proposal

1st Change

# Introduction

In the existing system it is a need that the “job reference” (e.g. Trace Reference for TraceJob, jobId for PerfMetricJob and qoEReference for QMCJob) is unique within a PLMN so that the producer can send the requested data to the right consumer.

In the existing system it is the consumers that sets the “job reference”. With a number of consumers that are separated from each other, it is not possible to fulfil the requirement of uniqueness, as the consumers can be different Network Functions (NFs) as well as different MnFs (Management Function).

With an increasing number of consumers, it is likely that the same data is requested by different consumers. It is investigated whether the NF needs to capture those data several times or if the reporting to different consumers can be moved out from the NF without any significant drawback.

2nd Change

## 3.3	Abbreviations

For the purposes of the present document, the abbreviations given in 3GPP TR 21.905 [1] and the following apply. An abbreviation defined in the present document takes precedence over the definition of the same abbreviation, if any, in 3GPP TR 21.905 [1].

MnF	Management Function

NF	Network Function

End of Change