# 3GPP TSG-SA5 Meeting #154	S5-242097

# 15 - 19 April 2024, Changsha, Hunan, China

# Source:	Nokia

# Title:	Training Data Statistical Properties

# Document for:	Approval

# Agenda Item:	6.19.1

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	Rationale

This pCR is to add a new use case, potential requirements and a potential solution on training data statistical properties for ML training. This pCR is motivated from TS 23.288 (SA2) where the consumer of the Nnwdaf_AnalyticsSubscription_Subscribe or Nnwdaf_AnalyticsInfo_Request service operations provides “Dataset Statistical Properties” as an input parameter to influence the training data selection mechanisms by the NWDAF. The two attributes under dataset statistical properties specified include: (i) Uniformly distributed datasets, (ii) Datasets with or without outliers.

# 3	Detailed proposal

Start of modification

## 5.X	Management Capabilities for ML training

## 5.X.1			Use Cases

5.X.1.1		Training data statiscal properties for ML training

Non-uniform distribution of training data can significantly degrade the performance of trained ML entities. The ML entity may learn and reflect this non-uniformity, rather than the true underlying patterns in the data. This could lead to inaccurate decisions when the ML entity is deployed for inference. Furthermore, an ML entity trained on non-uniform data may not generalize well to new unseen data, as the training data might not accurately represent the full range of possible inputs the ML entity may encounter during inference. This can limit the usefulness of the ML entity.

Similarly, outliers in training data can significantly degrade the performance of trained ML entities. ML entities learn to make decisions based on the patterns they identify in the training data. Outliers can skew these patterns and lead to an ML entity that is biased towards these extreme values, rather than accurately reflecting the majority of the data.

Therefore, it is crucial to ensure that training data is as uniform and representative as possible, and outliers are handled appropriately during the data preprocessing stage so as to train robust ML entities that do not require frequent re-training.

Furthermore, if the number of training data samples used to train an ML entity is significantly low, the ML entity may not represent the overall problem for which it is trained for, although the ML entity performance may be good.

### 5.X.1.2			Potential requirements

REQ-DATA-STAT-1: The 3GPP management system should enable an authorized consumer to provide information on the training dataset distribution that the ML Training MnS producer should take into account for training an ML entity.

REQ-DATA-STAT-2: The 3GPP management system should enable an authorized consumer to provide information on the usage of outliers in the training dataset that the ML Training MnS producer should take into account for training an ML entity.

REQ-DATA-STAT-3: The 3GPP management system should enable the ML Training MnS Producer to report on the number of training data samples used to train an ML entity to an authorized consumer.

### 5.X.1.3			Possible solutions

1) Introduce a new attribute of type, e.g., datasetStatisticalProperties, in the MLTrainingRequest IoC requested by an authorized MnS Consumer to the ML Training MnS Producer. This information influences the training data selection mechanisms to be used for training an ML entity, assuring that the trained ML entity reflects the statistical characteristics of the data that are relevant for the inferenceType. The proposed datasetStatisticalProperties datatypemay include the following two attributes:

- UniformlyDistributedTrainingData - It indicates the need for using training data that are uniformly distributed according to the different aspects of the inferenceType. The attribute is of type Boolean. For e.g., in case of coverage problem analytics, data samples for gNBs belonging to each geographical location area needs to be uniformly distributed for the ML entity to correctly determine in which geographical location areas the coverage problem occurred during inference.

- TrainingDataWithOrWithoutOutliers – It indicates that the training data samples shall consider or disregard data samples that are at the extreme boundaries of the value range. The attribute is of type Boolean. For e.g., in case of coverage problem analytics, if there are only say few training data samples belonging to a particular geographical location, they may be considered as outliers w.r.t. the other training data samples.

2) Introduce a new attribute e.g., NumberOfTrainingDataSamples in the MLTrainingReport IoC reported by the ML Training MnS Producer to an authorized MnS Consumer after the ML entity has been trained.

End of modifications