3GPP TSG-SA5 Meeting #154 	S5-242113d2

Changsha, China, 15 April - 19 April 2024

# Source:	China Telecom, DTAG

# Title:	New use case to support management of Core Network Function(s) on-board satellite(s)

# Document for:	Approval

Agenda Item:	6.19.15

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]	3GPP TR 23.700-29: " Study on integration of satellite components in the 5G architecture Phase 3".

[2]	3GPP TS 28.541: "Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3".

# 3	Rationale

In Rel-19, SA2 has started a study TR 23.700-29 [1] on supporting of UE-satellite-UE communication under regenerative-based satellite access architecture. The definition of UE-satellite-UE communication is as follows.

--- Start of quote from TR 23.700-29 ---

UE-satellite-UE communication refers to the communication between UEs under the coverage of one or more serving satellites without the user plane traffic going through the ground network.

---End quote---

To support UE-satellite-UE communication for IMS voice and video as well as MCPTT services, 5GC network function(s) is necessary onboard the satellite(s), e.g. UPF. After three meetings, all solutions addressing Key Issue #3 required UPF on-board satellite.

Observation 1: For realizing UE-satellite-UE communication, SA2 requires the network to support the operation of the UPF on-board satellite.

The previous SA5 work 5GSATB_OAM did not fully support the operation of UPFs on-board satellites. This is because the previous work was based on the satellite backhaul architecture, so the information of the UPF on-board satellite was only configured in the backhaul information, as seen in TS 28.541 [2]. Therefore, using the existing information does

--- Start of quote from TS 28.541---

5.3.231	SatelliteBackhaulInfo <<dataType>>

5.3.231.1	Definition

This datatype defines information related to satellite backhaul category and corresponding information of (R)AN.

5.3.231.2	Attributes

| Attribute name | S | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |
| nTNGlobalRanNodeID | M | T | T | F | T |
| satelliteBackhaulCategory | M | T | T | F | T |
| geoSatelliteId | CM | T | T | F | T |

5.3.231.3	Attribute constraints

| Name | Definition |
| --- | --- |
| geoSatelliteId S | Condition: Present if UPF is deployed on a GEO satellite. NOTE 1: In the present document, only the feature of deploying UPF on GEO satellite is supported. |

5.3.231.4	Notifications

The subclause 5.5 of the <<IOC>> using this <<dataType>> as one of its attributes, shall be applicable.

---End quote---

Observation 2: The existing SA5’s work cannot cover this use case.

Based on the above observations, we found that to support UE-Satellite-UE communication, 3GPP management system needs to be enhancement to support management of Core Network Function (e.g. UPF) on-board satellite.

Proposal: NRM enhancements need to be investigated to manage the Core Network Function (e.g. UPF) on-board satellite.

# 4	Detailed proposal

Start of 1st Change

## 5.X UE-Satellite-UE communication

### 5.X.1 Use case #1 UE-Satellite-UE Communication via UPFs on-board the satellites

#### 5.X.1.1 Description

SA2 R19 work has specified the requirement for architectural enhancements, including core network functions on-board satellite, to support new communication mode or service, such as UE-Satellite-UE. This introduces new management requirements, for example, when UPF on-board satellite and SMF on the ground, the N4 associations change frequently. So, the UPF and/or SMF need to know when to establish and release the N4 associations with which SMF and/or UPF. Another example, to support UE-satellite-UE communication, 3GPP management system configures indication information (i.e., indicates whether UPF is on-board satellite or not) enabling the SMF to know which UPF is on-board satellite. Thus, the UPF on-board satellite is selected to keep user plane traffic remain in the satellites.

An example diagram of the gNB and UPF deployed on satellite to enable UE-Satellite-UE is shown in Figure 5.X.1.1-1.

Figure 5.X.1.1-1: UE-Satellite-UE Communication via UPFs on-board the satellites

#### 5.X.1.2 Potential requirements

REQ- FS_NTN_OAM_Ph2-1：3GPP management service producer should have the capability to configure the  associations between UPF on-board satellite and SMF on the ground .

REQ- FS_NTN_OAM_Ph2-2：3GPP management service producer should have the capability to configure the UPF or SMF enabling the SMF to know which UPF is on-board satellite.