3GPP TSG-SA5 Meeting #154 	S5-242134d1

Changsha, China, 15 - 19 April 2024

# Source:	China Unicom

# Title:	pCR 28.878 Concepts and background

# Document for:	Approval

Agenda Item:	6.19.19

# 1	Decision/action requested

The group is asked to discuss and approve.

# 2	References

[1]	3GPP TR 28.878 v0.0.0 Study on management of network sharing phase 3

# 3	Rationale

This contribution proposes to add text for Clause 4 Concepts and overview in [1].

# 4	Detailed proposal

It proposes to make the following changes to TR 28.878 [1].

1st Change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[y1]	3GPP TS 22.261: "Service requirements for the 5G system".

[y2]	3GPP TR 22.851: "Feasibility Study on Network Sharing Aspect".

[y3]	3GPP TS 32.130: "Network sharing; Concepts and requirements".

2nd Change

# 4	Concepts and background

Network sharing is a crucial approach to decrease CAPEX of 5G constructions for operators. As stated in TS 22.261[y1] the increased density of access nodes needed to meet future performance objectives pose considerable challenges in deployment and acquiring spectrum and antenna locations. RAN sharing is seen as a technical solution to these issues. Plenty of previous normative works have been completed during Rel-17 and Rel-18.

During Rel-18, SA5 has specified new scenarios for MOCN Network sharing, SBMA deployment examples for MOCN management architectures and related NRM enhancements in TS 32.130[y3]. Some leftover issues for existing MOCN, including Trace job and collection requirements for POPs, etc., are supposed to be further studied.