3GPP TSG-SA5 Meeting #154 	S5-242135d1

Changsha, China, 15 - 19 April 2024

# Source:	China Unicom

# Title:	Add use case, requirements for Service-based management architecture and access requirements for MOCN

# Document for:	Approval

Agenda Item:	6.19.19

# 1	Decision/action requested

The group is asked to discuss and approve the proposals.

# 2	References

[1]	3GPP TR 28.878 Study on Management of Network Sharing Phase 3

[2]      3GPP TR 28.835 Study on Management Aspect Enhancement of 5G MOCN Network Sharing Phase2

# 3	Rationale

It was approved to study Management of Network Sharing Phase 3 [1]. In Rel 18, there still remain some leftover issues that have not been resolved. In TR 28.835[2], Issue #4: Service-based management architecture for MOCN and Issue #5: Use of MSAC for MOCN sharing scenarios should be studied further.

# 4	Detailed proposal

This contribution proposes to make the following changes in [1].

1st Change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[X]      3GPP TR 28.835: "Study on Management Aspect Enhancement of 5G MOCN Network Sharing Phase2".

2nd Change

## 5.X	Use Case#X: Service-based management architecture and access requirements for MOCN

### 5.X.1	Description

In TR 28.835[X] of Rel 18, there are some remaining issues that need to continue to study, including Issue #4: Service-based management architecture for MOCN and Issue #5: Use of MSAC for MOCN sharing scenarios.

The Service Based Management Architecture (SBMA) need to be provided for MOCN networking sharing. But the potential solution is an example of the service-based management architecture for MOCN, and the comprehensive service-based management architecture needs further study.

The management system of MOP should have the capability to allow authorized POP users to access, read and download data of configuration, performance measurements and alarms. Therefore, some potential solutions of users’ access and relevant system user permissions for each POP need to be studied.

### 5.X.2 Potential requirements

REQ-NetShare_Config-1: The MOP MnS producer should support MnS consumer to request to access the MOP management system.

REQ-NetShare_Config-2: The MOP MnS producer should allow or forbid MnS consumer to obtain configuration, performance measurements and alarm data.

REQ-NetShare_Config-3: The MOP MnS producer should support roles for each POP as MnS consumers.

End of Changes