3GPP TSG-SA5 Meeting #154 	S5-242136d1

Changsha, China, 15 - 19 April 2024

# Source:	China Unicom

# Title:	Add use case, requirements for Trace job and collection requirements for POPs

# Document for:	Approval

Agenda Item:	6.19.19

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

[1]	3GPP TR 28.878 Study on Management of Network Sharing Phase 3

# 3	Rationale

It was approved to study Management of Network Sharing Phase 3 [1]. One of the objectives of this new study item is studying the trace job and collection requirements for POPs. For supporting the POP’s network operation, the different trace data or performance data with collection time window, collection requirements, etc., should be reported for each POP.

# 4	Detailed proposal

This contribution proposes to make the following changes in [1].

1st Change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[X]      3GPP TS 28.622: "Generic Network Resource Model (NRM);Integration Reference Point (IRP); Information Service (IS)".

2nd Change

## 5.X	Use Case#X: Trace job and collection requirements for POPs

### 5.X.1	Description

For 5G MOCN Networking Sharing, different POPs require different data for personalized operation and maintenance services, including collecting different trace and performance data requirements. For example, the different trace data or performanced data with collection time window, collection requirements, etc., should be reported for each POP.

The existing specifications do not provide some descriptions of trace job, collection flows and interface details for NG-RAN MOCN network sharing scenario. Therefore, some potential solutions of trace job and collection requirements for POPs need to be studied.

### 5.X.2 Potential requirements

REQ-NetShare_TraceConfig-1:The 3GPP management system of the MOP should have the capability to support operator-specific management data collection jobs.

End of Changes