# 3GPP TSG-SA5 Meeting #154	S5-242144

# 15 - 19 April 2024, Changsha, Hunan, China

# Source:	China Mobile, Ericsson, NEC, CATT

# Title:	Rel-19 Add use case of ML pre-training

# Document for:	Approval

# Agenda Item:	6.19.1

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1] 	3GPP TR 28.908-018 “Study on Artificial Intelligence/Machine Learning (AI/ ML) management”.

[2] 			3GPP TR 28.9xx-00 “Study on Artificial Intelligence/Machine Learning (AI/ ML) Lifecycle Management (LCM) Phase 2”.

# 3	Rationale

The ML pre-training gives a chance for consumer to generate the first version of an ML model without the indication of inference type. A pre-trained ML model would be efficiently used by fine-tuning to fast generate ML model for specific downstream tasks.

# 4	Detailed proposal

Start of modification

# X	Use cases, potential requirements and possible solutions

## 5.1	Management Capabilities for ML training

5.1.X 	 Pre-training for specific inference type

5.1.X.1 	Description

A pre-training is an ML training for training an ML model with domain related dataset but with dataset that covers more than one inference type.

The pre-training is not aimed to support a specific use case but focuses on communalities in use cases.

#### 5.1.X.2	Use cases

##### 5.1.X.2.a	consumer requested general ML training

The pre-training for an inference type may be triggered by request(s) from one or more consumer(s). The same procedure for ML training can be used for pre-training, however the information in training request is different.

##### 5a.1.X.3	Potential requirements

REQ-ML_ TRAIN -MLPT-1: The ML Training MnS producer shall have a capability to enable an authorized consumer to request a pre-training of an ML model for a specific inference type.

Note: The same requirements in existing TS 28.105 Table 6.2a.1.3-1 related to training function applies for pre-training.

END of modification

# Comments

Intel