# 3GPP TSG-SA5 Meeting #154	S5-242145

# 15 - 19 April 2024, Changsha, Hunan, China

# Source:	China Mobile

# Title:	Rel-19 Add use case of ML fine-tuning

# Document for:	Approval

# Agenda Item:	6.19.1

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1] 	3GPP TR 28.908-018 “Study on Artificial Intelligence/Machine Learning (AI/ ML) management”.

[2] 			3GPP TR 28.9xx-00 “Study on Artificial Intelligence/Machine Learning (AI/ ML) Lifecycle Management (LCM) Phase 2”.

# 3	Rationale

ML fine-tuning (MLFT) refers to train an ML model not from scratch by only training a small set of parameters which might be a subset of the existing model parameters or a set of newly added parameters. The ML model would be trained in a very efficient way and applied to specific tasks.

# 4	Detailed proposal

Start of modification

# X	Use cases, potential requirements and possible solutions

## 5.1	Management Capabilities for ML training

5.1.X 	ML fine-tuning

### 5.1.X.1 	Description

ML fine-tuning (MLFT) refers to train an ML model not from scratch by only training a small set of parameters which might be a subset of the existing model parameters or a set of newly added parameters.

In contrast to ML re-training (a re-trained ML model supports the same type of inference as the previous version), ML fine-tuning would give the chance to create, add or change the inference type for a ML model, which also suggests an ML model after several times fine-tuning could have multiple inference type, e.g. an ML model could handle with both FailurePrediction and CoverageProblemAnalysis [see TS 28.104].

The use case that a ML model request a ML fine-tuning process could be:

- to create an inference type for an ML model, e.g. pre-trained model;

- to add or change an inference type for an ML model.

#### 5.1.X.2	Use cases

5.1.X.1.1	ML fine-tuning for a pre-trained ML model

In this typical use case, a pre-trained ML model gains the pattern, relevance and structure of a domain but yet to handle with downstream tasks, i.e. there is no specific inferenceType. Therefore, the consumer would like to fine-tune such pre-trained ML model for the purpose of creation of a new inference type.

The consumer should have the capability to request ML fine-tuning. After ML fine-tuning, the producer should report the results of ML fine-tuning including the identifier, version number, the type of the model (e.g. fine-tuned), new added inference type, etc.

The consumer should have the capability to request for ML fine-tuning and manage the process of ML pre-training.

5.1.X.1.2	ML fine-tuning to add or change inference type

TBD.

##### 5.1.X.3	Potential requirements

REQ-ML_ TRAIN -MLFT-1: The MLT MnS producer shall have a capability to enable an authorized consumer to request the ML fine-tuning of an ML model.

REQ-ML_ TRAIN-MLFT-2: The MLT MnS producer shall have a capability to provide the fine-tuning results (including the identifier, version number, and the status indicator of the model (e.g. fine-tuned), etc).

REQ-ML_ TRAIN-MLFT-3: The MLT MnS producer shall have a capability allowing an authorized consumer to indicate the purpose of a ML fine-tuning process, e.g. to create, add or change the inference type.

REQ-ML_TRAIN-MLFT-4: The MLT MnS producer shall have a capability allowing an authorized MLT MnS consumer to manage the training process, including starting, suspending, or resuming the fine-tuning process, and configuring the ML context for ML fine-tuning.

END of modification