# 3GPP TSG-SA5 Meeting #154	S5-242145

# 15 - 19 April 2024, Changsha, Hunan, China

# Source:	China Mobile, Ericsson, NEC

# Title:	Rel-19 Add use case of ML fine-tuning

# Document for:	Approval

# Agenda Item:	6.19.1

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1] 	3GPP TR 28.908-018 “Study on Artificial Intelligence/Machine Learning (AI/ ML) management”.

[2] 			3GPP TR 28.9xx-00 “Study on Artificial Intelligence/Machine Learning (AI/ ML) Lifecycle Management (LCM) Phase 2”.

# 3	Rationale

ML fine-tuning refers to train an ML model not from scratch by only training a small set of parameters which might be a subset of the existing model parameters or a set of newly added parameters. The ML model would be trained in a very efficient way and applied to specific tasks.

# 4	Detailed proposal

Start of modification

# X	Use cases, potential requirements and possible solutions

## 5.1	Management Capabilities for ML training

5.1.X 	ML fine-tuning

### 5.1.X.1 	Description

ML fine-tuning refers to train an ML model (e.g. a pre-trained model) not from scratch by only training a small set of model parameters which might be a subset of the existing model parameters or a set of newly added model parameters.

In contrast to ML re-training (a re-trained ML model supports the same type of inference as the previous version), ML fine-tuning would give the chance to modify the inference type for a ML model.

#### 5.1.X.2	Use cases

5.1.X.1.1	ML fine-tuning for a pre-trained ML model

In this typical use case, a pre-trained ML model has been trained by the dataset that covers more than one inference type.

Therefore, the consumer would like to fine-tune a pre-trained ML model for the purpose of a specific inference type.

#### 5.1.X.3	Potential requirements

REQ-ML_ TRAIN-MLFT-1: The MLT MnS producer shall have a capability to provide the fine-tuning results (including the identifier, version number, and the status indicator of the model (e.g. fine-tuned), etc).

Note: The same requirements in existing TS 28.105 Table 6.2a.1.3-1 related to training function applies for fine-tuning.

END of modification