3GPP TSG-SA5 Meeting #154 	S5-242164

Changsha, China, 15-19 April 2024

# Source:	Rakuten Mobile

# Title:	pCR 28.869 New use case on data streaming for cloud native NFs

# Document for:	Approval

Agenda Item:	6.19.6

# 1	Decision/action requested

The group is asked to discuss and approve.

# 2	References

[1]	3GPP TR 28.869 v0.0.0 Study on cloud aspects of management and orchestration

[x]	3GPP TR 28.532: “Management and orchestration; Generic management services”

# 3	Rationale

This contribution proposes to add a new use case on data streaming for cloud native network functions.

# 4	Detailed proposal

It proposes to make the following changes to TR 28.869 [1].

1st Change

## 5.2	Use of industry solutions for management of cloud-native network functions

Editor's Note: This clause describes the use cases, issues, requirements, and solutions related to WT-2.

5.2.x	Use case #x: data streaming for cloud native network function 5.2.x.1	Description

Currently 3GPP management system support WebSocket based data streaming for PM, tracing and analytic [x] which establish point-to-point connection between the streaming data reporting MnS consumer and MnS producer. In cloud native deployment, a NF is realized in many micro-services whose workload instances are running in parallel, dynamically scaled in and out, and maybe distributed across multiple server nodes and cloud sites. Conventional WebSocket based data streaming solution is not suitable for cloud native deployment anymore. In conventional WebSocket based solution, streaming data reporting MnS producer aggregate traffic from many distributed workloads generating large amount of data before streaming it to the streaming data reporting MnS consumer via the connection established. The streaming data reporting MnS consumer receive the aggregated traffic first via the connection before distributing to internal functions of the management system which may be also cloud native. This become a performance bottleneck and is very inefficient. Furthermore, cloud native applications are more sensitive to failures and system down time. If the connection between MnS producer and consumer fails due to any reason e.g. software failure, server hardware failure and transport network failure etc, it impacts the entire coverage area of the cloud.

In cloud native deployment, more efficient, highly scalable, and fault-tolerant streaming solution allowing parallel streaming at the micro-service level may be needed. Furthermore, the management of streaming connections, resource allocations, scaling, and resiliency for data streaming in cloud native environment is a very complicated task. There are already industry solutions, e.g. Kafka and NATS, which was designed to tackle the challenges.  The 3GPP management system shall consider the adoption of these existing industry solutions.

### 5.2.x.2	Potential requirements

The 3GPP management system shall be able to handle the establishment of PM, tracing, or analytic data steaming sessions for cloud native NFs.

The 3GPP management system shall be able to handle the termination of PM, FM, tracing, or analytic data steaming sessions for cloud native NFs.

The 3GPP management system shall enable a cloudified NF to stream PM, FM, tracing, or analytic data to the 3GPP management system.

### 5.2.x.3	Potential solutions

### 5.2.x.4	Evaluation of solutions