3GPP TSG-SA5 Meeting #154	S5-242184

# Changsha, Hunan Province, China, 15th Apr 2024 - 19th Apr 2024

| CR-Form-v12.3 |
| --- |
| CHANGE REQUEST |
|  | 32.158 | CR | 0136 | rev | 1 | Current version: | 17.7.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Rel-17 CR 32.158 Clarify usage of information models |
| --- | --- |
| Source to WG: | Nokia |
| Source to TSG: | SA5 |
| Work item code: | REST_SS, TEI17 |  | Date: | 2024-04-05 |
| Category: | F |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) … Rel-17 (Release 17) Rel-18 (Release 18) Rel-19 (Release 19) Rel-20 (Release 20) |
| Reason for change: | The usage of information models as specified now misses two important aspects: They provide constraints on the structure of information on the MnS Producer. They provide constraints on the possibilities to update information on the MnS Producer. |
| Summary of change: | The missing aspects are added. |
| Consequences if not approved: | The information models might be used only as message models but not as the definition of valid object trees on MnS Producers. |
| Clauses affected: | 4.1.5 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: | S5-241423 |

Begin of modifications

### 4.1.5	Usage of information models

Information models are used for two purposes when specifying interfaces to observe and act upon information models:

-	They provide a means to identify information in request messages.

-	They provide a format to transfer information in request and response messages.

-	They provide constraints on the structure of information on the MnS Producer.

-	They provide constraints on the possibilities to update information on the MnS Producer.

Identification of information is necessary when retrieving information from a MnS Producer; the MnS Consumer needs to be able to specify in his retrieveal request the information the MnS Producer shall return. But also when information needs to be updated or deleted the MnS Consumer needs to identify the information to be updated or deleted in his request. When information is added, the location of the new information is specified relative to the location of existing information.

Request and response message bodies carrying (some parts of) the information model are also constructed based on the information model supported by the MnS Producer. The message format is either identical to the information model format or identical to some transformation of the information model format.

End of modifications