## Slide 1
Source: Rakuten Mobile Inc.
Multipoint-to-Multipoint Data Reporting in SBMA based on Message Bus

## Slide 2: Background and Motivation
Existing 3GPP SA5 support only point-to-point data reporting between MnS producer and MnS consumer
MnS consumer discovers the service produced by a MnS producer and the management data reporting capability from MnsRegistry (TR 28.842, TS 28.622)
The MnS consumer then creates instances of IOC PerfMetricJob to the MnS producer.
Then point-to-point data reporting starts between the MnS producer and the MnS consumer based on the streaming data reporting service or file data reporting service (TS 28.532)
There are scenarios where multipoint-to-multipoint communication is needed among MnFs which allows data to be shared across multiple MnS consumers.
5GA Rel20 SBMA SID has captured work task to study how to support the multipoint-to-multipoint data communication in SBMA
MnF
Shared data bus
MnF
MnF
MnF
MnF
MnF

## Slide 3: Example use case using multipoint-to-multipoint communication
AIML LCM
Shared data bus
Service Assurance
NFMF
Analytic
NDT
External consumer
NFMF
PM/FM data collected by NFMF is published and consumed by multiple MnFs e.g. AIML LCM, service assurance, analytics, NDT related MnFs.
Through the shared data bus, each MnF discovers, subscribes to and receives its own copy of the data.
The data producers and data consumers in each MnF are decoupled by the data framework middleware layer and can be scaled independently.
Data can be exposed to or produced by external consumers also.

## Slide 4: Potential Solution – New MnSs
Data Management MnF
Message Broker
MnF
Data publishing MnS
MnF
…
MnF
Data consuming MnS
MnF
Data consuming MnS
…
Data publishing MnS
Data discovery MnS
Data subscription MnSs
Data registration MnSs
Data job control MnSs
Data Registry
MnS Registry
New services to be defined
Data producing MnFs register supported data reporting capabilities and data types to Data Management MnF via data registration related MnSs.
Data consuming MnFs discover the registered data types and reporting capabilities via data discovery related MnS before subscribe to the data via data subscription related MnSs.
Data Management MnF creates data jobs in the data producing MnFs via data job control related MnSs and triggers them to start data reporting via data publishing MnS
Data consuming MnFs receive data via data consuming MnS.

## Slide 5: Conclusion (to be endorsed)
Agree in principle the problem statement (supporting multipoint-to-multipoint communication in SBMA) in page 2.
Add a section in Rel20 SBMA TR 28.884 to further study key issues, use cases and potential requirements for enabling multipoint-to-multipoint data communication in SBMA.
Study the potential solutions and documented in the section.