## Slide 1: EDGE on-board NGSO Satellite
Discovery and Service Provisioning
(KPN N.V.)

## Slide 2: Problem: Key Issue 5 Edge on-board the satellite
NGSO satellites are satellites moving with respect to the earth surface and they can be deployed in MEO (8,000 km – 20,000 km ) or LEO (400 km – 2000 km) orbits. When you have Edge on board satellite.
  Advantage: Reduce Latency
  Challenge: the Edges are now moving with respect to the earth
The discovery and the service provisioning now can now be better optimized by selecting Edge on-board a satellite that closely match the movement of the UE which hosts the AC and the EEC.

## Slide 3: Service Provisioning and Discovery of Edge on-board and the UE
The EAS and EES will now have trajectory that is the same as the trajectory of the satellite it is onboard on.
Depending on the route and planned route of the UE different EAS and EES may be more suitable.

## Slide 4: 1. Satellite Trajectory: inputs
Satellite Type + Orbital Parameters (e.g. altitude, inclination, eccentricity ..)
Satellite LTE (two-line element set): data format encoding a list of orbital elements of an Earth orbiting object for given point in time, the epoch. (Satellite catalog number, epoch, mean motion and its derivative , drag term, ephemeris type, eccentricity, argument of perigee, mean anomaly, mean motion. (LTE based mean orbital ephemeris)
Ephemeris: table giving the coordinates of a celestia body at specific time during a given period. The most precise but also changes frequently. (instantaneous/osculating ephemeris)
This information does not give you location or current trajectory of satellite. Based on this information the position and the trajectory of the satellite need to be calculated.

## Slide 5: 1. Satellite Trajectory: Position and Trajectory of the satellite
Calculating the position of the satellite based on Ephemeris is:
  Complex process
  Time dependent
On top of this the Ephemeris it self changes frequently and it is updated.
The updated information exist with the Satellite Provider and/or the Operator.
This is best done by the Satellite Provider and/or the Operator and so it is best to leave that problem to them.
EEL we provide the a Trajectory ID and how the Trajectory ID is mapped to the actual Ephemeris information is up to the Satellite Provider and/or operator.

## Slide 6: 1. Satellite Trajectory: Trajectory ID
Satellite Service Provider and/or operator Server for Satellite Trajectory
EAS Profile: Trajectory ID
EES Profile:
Trajectory ID
Mapping
Trajectory ID : Trajectory information (real time) Ephemeris.
AC
Lets SA6 abstract away from the actual satellite position calculation and let it do what it is good at (EDGEAPP). The satellites can do what they are good at that is calculating the current position of a the satellite which the EAS and the EAS on-boarded. And let the Trajectory ID serve as an ID which points in the server to a changing positional information no matter how they calculate it.

## Slide 7: 2. Route or Planned Route of the UE
In 23.558 we already have the Expected AC Geographic Service Area which tells you already expected location(s) (e.g. route) of the hosting UE.
The Expected AC Geographic Service Area is some kind of trajectory of the AC. However this is not related to the movement of the satellite. The Satellite Service Provider and/or the Operator Server which provided the Trajectory ID can also provide a Trajectory ID to the AC that best matches the movement
Information element | Status | Description
ACID | M | Identity of the AC.
Expected AC Geographical Service Area | O | The expected location(s) (e.g. route) of the hosting UE during the AC's operation schedule. This geographic information can express a geographic point, polygon, route, signalling map, or waypoint set.

## Slide 8: 2. Route or Planned Route of the UE
Similar with the Expected AC Geographic Service Area as Satellite Provider can provide an Expected Trajectory ID which is a trajectory ID which better maps the Expected AC Geographical Service Area. This can be provided by the same Satellite Service Provider and/or Operator Server which have assigned the Trajectory ID.
Information element | Status | Description
ACID | M | Identity of the AC.
Expected AC Geographical Service Area | O | The expected location(s) (e.g. route) of the hosting UE during the AC's operation schedule. This geographic information can express a geographic point, polygon, route, signalling map, or waypoint set.
Expected trajectory Id | O | The trajectory ID of a satellite that closely matches the expected AC geographical service area.

## Slide 9: Discovery and Service Provisioning
Satellite Service Provider and/or operator Server for Satellite Trajectory
EAS Profile: Trajectory ID
EES Profile:
Trajectory ID
AC Profile
Expected Trajectory ID that matches the “Expected AC Geographical Service Area”
Trajectory ID are related to Satellite information such as Satellite Ephemeris.
The AC profile is used both for Service Provisioning and Discovery, and the Trajectory ID is in the EAS profile and EES profile. Therefore with this change both Discovery and Service Provisioning can be performed.

## Slide 10: Mobility or Dynamic EDN
This procedure is important in case of the NGSO satellite where the EAS and EES move.
This introduces mobility or dynamic EDN.
This has to be indicated in the EAS and EES profile and trajectory ID and other relevant information in relation with this should be considered only when the EAS and EES are mobile.
Hence it is proposed to have Mobility. (also can be renamed to Dynamic EDN)