3GPP TSG-SA WG6 Meeting #60	S6-241058

Changsha , China, 15 Apr 2024 - 19 Apr 2024	(revision of S6-xxxxxx)

Source:	China Mobile

Title:	upate solution #7

Spec:	3GPP TR 23.700-82 v0.3.0

Agenda item:	8.3

Document for:	Approval

Contact:	           Xiaohui Shi, shixiaohui@chinamobile.com

1. Introduction

Update solution #7, in step 1,”A VAL server sends a request to an AIML enablement serve”, the flow chart is still AIML enablement consumer, these two places are inconsistent

2. Reason for Change

The flowchart and step description are inconsistent

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-82 v0.3.0.

* * * First Change * * * *

### 8.7.1	Solution description

The following clauses specify procedures, information flows, and APIs for Key Issue #3 to support AIML enablement client discovery.

Assumptions:

1.	The proposed solution is based on client-server architecture for federated learning.

2.	The AIML enablement server has a repository of AIML enablement clients and associated AIML client profiles.

3.	AIML enablement clients that support AIML operations have registered with the AIML enablement server and included their AIML client profile. The registration procedure may be performed as described in solution 8.

Figure 8.7.1-1: AIML client discovery procedure

1.	The AIML enablement consumer (e.g. A VAL server )sends a request to an AIML enablement server to discover AIML enablement clients that are available to participate in federated learning operations, e.g. is available and have required data to train an ML model. The AIML enablement client discovery request includes client/server identifier, security credentials, discovery criteria. The request may also include AIML task container to discover clients who can perform the AIML tasks like AIML model training/offload/split. The AIML task container includes required task service availability duration, AIML task type like model transfer, model training. The request may include a minimum number of FL members required for AIML operation splitting.

* * * End of Changes * * * *