## Slide 1: Bosch's View on 6G Study in RAN
Agenda Item 4: Vision & priorities for next generation radio technology
3GPP 6G Workshop
Incheon, South Korea, March 10-11, 2025
6GWS-250148

## Slide 2: Agenda
Evolving 5G Capabilities in 6G Timeframe
Use Case-Specific Local Subnetworking
Integrated Sensing and Communication (ISAC)
Enhancements for Distributed Automotive Functionalities
NTN Enhancements for Connected Mobility in 6G
Conclusion and Discussions

## Slide 3: Evolving 5G Capabilities in 6G Timeframe
Bosch View on 6G Study in RAN for Release 20
  Smooth evolution and backward compatibility with 5G is crucial for the RAN Rel-20 6G study, given the long lifecycle of automotive and industrial devices.
  The 6G RAN should support current 5G use cases and new ones, e.g., subnetworking, automated driving, distributed AI, digital twins, etc.
  The 5G Sidelink design should be the baseline for Sidelink enhancements in 6G, ensuring interoperability in V2X bands to avoid disrupting deployment plans.
  6G NTN should consider automotive use cases, without negatively impacting the current and upcoming commercial deployments based on 5G NTN.
  Resilient and accurate 6G positioning is essential for vertical use cases.
Evolution of the Existing Technologies
Smooth Migration and Backward Compatibility

## Slide 4: Use Case-Specific Local Subnetworking
Bosch View on 6G Study in RAN for Release 20
Required RAN Studies for Local Subnetworking in 6G
Local subnetworks for various verticals’ use cases have been discussed in SA1.
Potential RAN studies should consider the support of:
  Local management and configurations;
  Bulk resource allocation for subnetworks;
  Mobility of subnetworks and their devices;
  Enhancements/new interfaces.
Coordinated studies with SA WGs:
  Architecture enhancements and impacts on RAN;
  Support for security and trustworthiness aspects.
Proposal 1: Study on RAN level requirements to realize (partial) autonomous subnetworks
  Consider SA1 use cases and new service requirements
Parent network (e.g., PLMN)
Subnetworks

## Slide 5: Integrated Sensing and Communication
Proposal 2: ISAC initial study in Release 20 should focus on:
  gNB-side sensing
  Limit the study to FR2
Bosch View on 6G Study in RAN for Release 20
Required RAN Studies for ISAC in 6G timeframe
Possible ISAC use cases: sensing as a service (SaaS)
Study possible RAN impacts, including:
  Spectrum and bandwidth requirements;
  Protocols and signaling enhancements;
  RAN support for security, privacy & trustworthiness;
  Study relevant RAN KPIs, e.g., sensing accuracy.
Several modes could be studied, including:
  Mono-static vs Bi-static;
  gNB-side vs UE-side.
Sensing
receiver
Sensing target object
SaaS
Sensing
transmitter
Core Network
Sensing
Service

## Slide 6: Enhancements for Distributed Automotive Functionalities
Proposal 3: For reliable distributed Automotive functions, RAN should support:
  Mutual awareness between RAN and automotive functions/applications
  Protocol enhancements for jointly achieving low latency, high data-rate, high reliability, enhancing resilience and mobility
Bosch View on 6G Study in RAN for Release 20
Required Studies for Distributed/Offloaded Automotive Functions in 6G
Exemplary functional offloading use cases:
  Distributed automotive functions, i.e., off-board & on-board, e.g., ADAS, motion functions, maps, etc.;
  Offloading AI/ML computations, e.g., Net4AI with AI inference, to a trusted server or the cloud.
6G RAN should support:
  Introducing signaling for mutual awareness between automotive application and RAN;
  Protocol enhancements to jointly achieve the automotive required latency, reliability, rate, etc.;
  Increasing resilience and ensuring interruption-free mobility.

## Slide 7: NTN Enhancements for Connected Mobility in 6G
Proposal 4: For NTN automotive requirements, RAN should study the support of the following in 6G timeframe:
  Native support to automotive terminals and lower-latency mobility interruption (between TN/NTN, different NTN orbits)
  Dual traffic-steering and dual-/multi-connectivity (between TN/NTN, NTN/NTN)
  GNSS independent operation for positioning and timing services
Bosch View on 6G Study in RAN for Release 20
Required RAN Studies for NTN in 6G Timeframe
Exemplary NTN use case for automotive:
  Vehicle health/status continuous monitoring;
  Vehicle’s remote control.
6G RAN should study the support of:
  Various vehicles’ terminal types, e.g., passenger vehicles, trucks, off-road vehicles, etc., from the first 6G release;
  TN/NTN mobility enhancements, lowering interruption latency-budget;
  Dual traffic-steering, with terminals simultaneously connected to TN and NTN, NTN and NTN, etc.;
  GNSS independent, e.g., positioning/timing services.

## Slide 8
Conclusion and Discussions
6G RAN Views on Meeting the Needs of Industrial Verticals
Given the long lifecycle of vertical devices, it's crucial for 6G RAN to smoothly evolve and stay backward compatible with 5G. Study RAN requirements to enable partially autonomous subnetworks, focusing on resource management, mobility, and interface capabilities. To make faster progress in Rel-20 ISAC studies, start with gNB-based sensing and FR2. For distributed and offloaded automotive functions, RAN should support awareness between RAN and automotive applications to jointly improve reliability, reduce latency, and enhance mobility. NTN is the focus of the current automotive deployment efforts; 6G should consider automotive requirements from Day 1.