## Slide 1
China Telecom View on 6G SID
C1-256453

## Slide 2
1. CT Timeline
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
2024
2025
SA1 SI
2026
2027
2028
SA2 SI
SA3, SA5,
SA6 start discuss and approve SI
CT start discuss and approve SI
CT approve SI related to stage 2
It is recommended that CT WGs start to discuss SI that independent with stage2 from 2025 Q4, and SI should be approved before 2026 Q1.
The SI that related to stage2 should be approved after stable requirement and conclusion from stage2.

## Slide 3
2.1 Motivation
AI agent
Sensing service
Proposal: New Protocols for control plane, user plane and data framework need to be studied because of the new requirement in 6G
Requirement
Use cases and requirement for 6G in SA1 includes AI Agent in UE and Network AI agent.
Multiple AI Agent protocols developed by AI companies have been applied in different scenarios.
Agent in UE might have influence on Control Plane (NAS) and User Plane, Network AI agent might have influence on Control Plane and Data Framework.
Observation: Protocols for AI agent needs to be studied to fulfil different use cases and requirement in 6G
Localized Networks
Requirement:
6G new NAS mechanism put forward the requirement to design new protocols for the sensing signaling control, which requires the enhancement on control plane protocols.
The interaction between the Sensing Function and the 6G Data Framework NFs also requires new data framework protocols for sensing data collection and transfer.
Requirement
Customized networking with reconfigurable and programmable NFs and services;
Resource and services sharing for users in different network or moving between different networks;
Secure interactions such as service registration, service discovery, signal proxy, and traffic transmission between networks.
Observation: Protocol to fulfil the requirement for localized network needs to be studied, including control plane, user plane and data framework aspects.
Observation: New protocols shall be designed for sensing service, including the control plane protocols and data framework protocols.

## Slide 4
2.2.1 6G Potential Protocol: Control Plane-New NAS
In 6G system the NAS design should also inherently support connectivity services with considering very well-structured modularity.
In order to support beyond connectivity services in 6G system, new NAS functionality sets can be estimated and the corresponding NAS procedure need to be studied as well. The introduction of a new NAS functionality should have no impact on other NAS functionality.
It is necessary to study a future-proven method to support NAS transmission for beyond connectivity services, to meet the scalability and efficiency requirement.
In 6G core network the NAS delivery and transmission mechanism is to be defined, to work in coordination with RAN.
Requirement / Motivation
Considerations on Protocol
5G NAS functionality combination does not support well internal modularity which leads to coupling between different NFs.
This issue brings complexity to network operation, longer time to roll out new services, and also difficulty to cost control of UE implementation using different NAS functionality set.
The inadequate modularity may also lead to more communication delay and resource consumption regarding more and more new services may occur in the future.

## Slide 5
2.2.2 6G Potential Protocol: Control Plane-HTTP/3
Requirements for HTTP/3
High Connection Establishment Latency：HTTP/2 over TCP + TLS requires multiple round trips (RTT) to establish a secure connection, establishing a secure connection requires 2-3 RTT of latency
Head-of-Line Blocking (HoLB) Problem：TCP guarantees in-order delivery of the byte stream. If any single IP packet is lost in the network, the entire TCP connection halts and waits for that packet to be retransmitted.
Poor Network Switching and Connection Migration Capability：A TCP connection is uniquely identified by a four-tuple If the IP address of either endpoint changes (e.g., a network element instance fails), the existing TCP connection breaks completely.
Inflexible Congestion Control：HTTP/2 relies on the underlying TCP's congestion control (e.g., CUBIC, BBR). TCP's congestion control is applied to the entire connection and cannot set different priorities or policies for different streams.
Advantages of HTTP/3 over HTTP/2:
Faster Connection Establishment: HTTP/3 utilizes the QUIC transport protocol, which operates over UDP. It combines the transport and cryptographic handshakes into a single step, significantly reducing round-trip times (RTT) during connection setup.
Reduced Latency and Improved Performance: HTTP/3 demonstrates superior performance under unreliable network conditions, such as high packet loss. It eliminates HoLB at the transport layer, enabling multiple streams to be transmitted concurrently without mutual interference.
Advanced Congestion and Flow Control: The built-in QUIC protocol employs modern congestion control algorithms that adapt efficiently to varying network conditions. It supports both connection-level and stream-level flow control, improving overall network.
Advanced Congestion Control: QUIC uses a Connection ID (CID) to uniquely identify a connection, which is independent of IP addresses. When IP change occurs, the connection can migrate seamlessly without any handshake as long as the client and server can maintain the same Connection ID.
Proposal：HTTP/3 should be considered for 6G Control Plane

## Slide 6
2.2.3 6G Potential Protocol: User Plane
Requirement / Motivation
Consideration on Protocol
Existing Challenges for 5G User Plane Protocol
  Stateful Tunnels: GTP-U necessitates that nodes maintain state for each tunnel. This adds complexity and hinders scalability as the number of devices and services grows.
  Limited Programmability: The fixed, per-tunnel paths of GTP-U make it difficult to implement advanced traffic engineering or dynamic service function chaining (SFC).
Enhanced GTP-U:
  Concept: Adds enhancements to the existing protocol to address limitations.
  Pro: Leverage existing 5G infrastructure.
  Con: May not be flexible enough to meet future 6G demands.
SRv6
  Concept: Shifts routing intelligence from the network to the packet source.
  Pros:
    High Programmability: Potential traffic engineering and service function chains by simply manipulating the Segment list.
    Enhanced Scalability: SRv6's stateless for support a massive number of devices and diverse services.
  Cons: Requires a significant paradigm shift from the current network architecture.
Proposal：User Plane Protocols for 6G need to be studied and evaluated to resolve the challenges faced in 5G
To resolve the challenges mentioned above, some potential user plane protocols are listed in the following:

## Slide 7
2.2.4 6G Potential Protocol: Data Framework
In 5G system, AI related data is collected via following protocols, and no unified protocol is used for data collection.
  Data from NFs via SBI using http/2.
  Data from UE via user plane using GTP-U, LPP
For large data transmission, QUIC is proposed as a potential protocol for its high transmission efficiency and high security, but it is less in compatibility.
For data access of high real-time demands and large data amounts, data protocols based on RDMA technology—such as RoCE—may be considered. These protocols possess zero-copy feature to achieve ultra-low latency and high-throughput performance, though they also exhibit greater hardware dependency.
Data from different sources, serving different purposes, may have distinct transmission requirements., e.g. security requirement, efficiency requirement, real-time requirement, resulting in a diverse demand for data protocols. Hence, the negotiation mechanism for data protocols between data providers and consumers might be considered.
Proposal: Analyze the specific use cases first and then determine the applicable protocol.
Requirement / Motivation
Consideration on Protocol
A large amount of data transferred in 6GS, e.g. sensing data, AI data, existing protocol has low efficiency on large amount data transmission.
Potential data sources, including UEs, NFs, OAM, RAN, 3rd party.
More requirement on data security and user privacy.

## Slide 8
3. Advice for CT1 -1
In CT1, we promote the study of PLMN Selection for DualSteer Device in 6G :
    Study whether and how to enhance the procedure to support the PLMN selection for the DualSteer Device, including:
      possible enhancement on the current information related to the PLMN selection, which are stored in the USIM, ME, or both;
      possible enhancement on the procedure of the first and the second PLMN selection for the DualSteer Device; and
      possible enhancement on NAS protocol for the DualSteer Device to support PLMN Selection.
It is recommended that CT WGs start to discuss SI that independent with stage 2 from 2025 Q4, but different CT WGs should to be coordinated to avoid redundant and clashing work, and also avoid approving SI without clearly requirement.
In CT1, 6G PLMN Selection (e.g. for DualSteer Device) study, 6G Secure SMS study, 6G UE-autonomous NAS parameters/procedures setting study, 6G NAS protocol study…
General Advice
Advice for 6G PLMN Selection study

## Slide 9
3. Advice for CT1 -2
In CT1, we promote the study of 6G Secure SMS:
    Study possible ways to build up the mechanism to support secure SMS, including:
      Study what the central functions should be included.
      Study possible ways to verify the identity of the SMS sender.
      Study how to add sender verification and integrity protection to SMS message.
      Study how to support displaying additional information (e.g. brand name, logo, etc.) of the SMS sender.
Advice for 6G Secure SMS study
Advice for 6G UE-autonomous NAS parameters/procedures setting study
In CT1, we support the study of 6G UE-autonomous NAS parameters/procedures setting:
    Problem statement :
      NAS procedures since 2G have been governed rigidly by fixed number of retries and timers which are set in the specification or signaled by the network.
      In some scenario, some NAS procedure seems not needed or meaningless.(e.g. repeated re-registration procedure for VoWifi case)
    Proposal:
      Integrate into the 6G NAS framework a mechanism to allow the UE to autonomously adjust the values of of retries and timers, and some procedure based on local information.

## Slide 10
THANK YOU