## Slide 1
3GPP TSG RAN Meeting #109
Beijing, China, September 15-18, 2025
Agenda Item: 8.2.1.2
Source: Samsung
Title: Samsung Views on IMT-2030 TPRs
Document for: Discussion
RP-251956

## Slide 2
Introduction
In RAN#108, 3GPP TSG RAN proposed to consider 4 additional items, i.e., positioning, sensing-related capabilities, AI-related capabilities, and joint/composite requirement, as IMT-2030 TPRs. Furthermore, 3GPP TSG RAN has held an initial discussion on target values for the listed TPR items and made some progress, as captured in RP-251825.
In this contribution, we provide the following for further discussion.
  Views on the TPR subjects pending from RAN#108
  Proposal on resilience
  Views on values of legacy TPRs
  Views on other TPRs
  Views on evaluation configurations

## Slide 3
Samsung Views on the TPR Subjects Pending from RAN#108
Peak data rate: It is preferred to define a requirement with a reasonable value. (same as Alternative 2 in moderator’s summary of CC#1 and CC#2, RP-251394)
Mobility interruption time: It is preferred to define a requirement as in IMT-2020.
Coverage: It is preferred not to define a requirement but to use the link budget template similar to IMT-2020 submission. (same as Option 2 in RP-251394)

## Slide 4
Proposed Definition for Resilience
Proposed revision (yellow-highlighted) based on the latest text from ITU-R WP 5D#49 (Annex 5.14 to Document 5D/792).
4.17 Resilience
(Editor’s note: This may also include Extended Connectivity)
Resilience refers to capabilities of the networks and systems to continue operating correctly during and after a natural or man-made disturbance, such as the loss of primary source of power, etc.
The RIT/SRIT should support functionalities over the radio interface that enable continuous operation or rapid temporary restoration during and after disturbance to radio infrastructure. These functionalities may include, but are not limited to, support for connecting to one or more of the following network infrastructures within the terrestrial component of IMT, which are temporarily operated to enhance connectivity during these situations:
‒ HIBS
‒ [Advanced] relays and repeaters
‒ Base station onboard a vehicle, airship and/or vessel
‒ Shared network infrastructures
‒ or other mechanisms for resilience using network infrastructures within the terrestrial component of IMT

## Slide 5
Samsung Views on Values of Legacy TPRs
# | TPRs | IMT-2020 Target (Reference) | RAN#108 Status | Samsung Proposal | Notes
1 | Peak data rate (Gbit/s) | DL: 20 UL: 10 | DL: TBD UL: TBD | [1.5x] | It is preferred not to overemphasize this item considering practicality and the absence of commercial use cases requiring high peak data rate.
2 | Peak spectral efficiency (bit/s/Hz) | DL: 30 UL: 15 | DL: TBD UL: TBD | [1.5x] | 1024 QAM (~25% over 256 QAM), 8/4 layers for DL/UL, overhead reduction compared to IMT-2020 (~30% to 20%).
3 | 5th percentile user data rate (Mbit/s) | DL: 100 UL: 50 | DL: TBD UL: TBD | DL: [4x] UL: TBD | DL: Enhanced average spectral efficiency and/or wider bandwidth UL: It is proposed to set target values after discussion on UL evaluation configurations.
4 | 5th percentile user spectral efficiency (bit/s/Hz) | Indoor Hotspot-eMBB (DL/UL): 0.3/0.21 Dense Urban-eMBB (DL/UL): 0.225/0.15 Rural-eMBB (DL/UL): 0.12/0.045 | Indoor Hotspot-IC: (DL/UL): 0.9/TBD Dense Urban-IC (DL/UL): 0.675/TBD Rural-IC (DL/UL): TBD/TBD | DL: [3x] UL: [3x] | Larger number of antenna elements than those used for IMT-2020
5 | Average spectral efficiency (bit/s/Hz/TRxP) | Indoor Hotspot-eMBB (DL/UL): 9/6.75 Dense Urban-eMBB (DL/UL): 7.8/5.4 Rural-eMBB (DL/UL): 3.3/1.6 | Indoor Hotspot-IC: (DL/UL): 27/TBD Dense Urban-IC (DL/UL): 23.4/TBD Rural-IC (DL/UL): TBD/TBD | DL: [3x] UL: [3x] | 
6 | Area traffic capacity (Mbit/s/m2) | 10 in Indoor Hotspot-eMBB | TBD in Indoor Hotspot-IC | [4x] | Enhanced average spectral efficiency and/or wider bandwidth
7 | User plane latency (ms) | eMBB: 4 URLLC: 1 | IC: 4 HRLLC: 1 | Fine with RAN agreement | IMT-2020 target has not been a bottleneck for commercial deployments.
8 | Control plane latency (ms) | 20 | 20 | Fine with RAN agreement | Could be reduced to 10 ms with 2-step RACH (Rel-16) or potential enhancements such as RACH-less approach for IMT-2030
9 | Connection density (devices/km2) | 106 | 106 | Fine with RAN agreement | IMT-2020 target has not been a bottleneck for commercial deployments.
10 | Reliability | 1-10-5 | 1-10-5 | Fine with RAN agreement | IMT-2020 target has not been a bottleneck for commercial deployments.
11 | Mobility (bit/s/Hz@km/h) | Indoor Hotspot-eMBB: 1.5@10 Dense Urban-eMBB: 1.12@30 Rural-eMBB: 0.8@120, 0.45@500 | Indoor Hotspot-IC: 2.25@10 Dense Urban-IC: 1.68@30 Rural-IC: [0.8-1.2]@120, [0.45-0.675]@500 | Rural-IC: [1.5x]@120, [1.5x]@500 | 
12 | Mobility interruption time (ms) | 0 | TBD | 0 | 
13 | Bandwidth (MHz) | 100 | 400 | Fine with RAN agreement | 

## Slide 6
Samsung Views on Other TPRs
# | TPRs | IMT-2020 Target (Reference) | RAN#108 status | Samsung Proposal | Notes
14 | Energy efficiency (%) | Sleep ratio and sleep duration (Inspection) | TPR (Exact definition TBD) | Relative network energy saving gain: [TBD] % Relative device energy saving gain: [TBD] % | Metric: Relative energy saving gain (in %) for unloaded case. Evaluation: Analytical evaluation for the unloaded case only is preferred. Power model: Proponents should report the power model used for the evaluation.
15 | Positioning (m) | N/A | Quantitative TPR (Target accuracy TBD) | Indoor Factory-ISAC (H/V): [0.5-1]/[1-3] for 90% of UEs Urban Macro-ISAC (H/V): [3]/[3] for 90% of UEs | Target positioning accuracies may not necessarily be reached for all scenarios and deployments. Necessity of vertical accuracy needs further discussion.
16 | Sensing-related capabilities | N/A | TPR (Exact definition TBD) | Detection/False alarm probabilities [%]: [95/5] Localization accuracy [m]: [1-5] @[95%] confidence level Velocity accuracy [m/s]: [1-5] @[95%] confidence level Resolution: TBD | ITU-R WP 5D agreed to define target values for detectability/false alarm probability, localization accuracy, velocity accuracy, keeping resolution TBD. It should be noted that the target sensing-related requirements may not necessarily be reached for all scenarios and deployments, depending on assumptions for sensing resources (e.g., bandwidth, power, number of antennas, and overhead, etc.)
17 | AI-related capabilities | N/A | Qualitative TPR (Inspection) | Fine with RAN agreement | 
18 | Composite requirement | N/A | KPI related to data rate, latency, reliability, capacity. Name may change. | Data rate (DL/UL): [30/10] Mbps Latency (DL/UL): [10/30] ms Reliability (DL/UL): [99/99] % Number of users per TRxP: [10] users w/ 90% satisfaction ratio | Quantitative TPR for immersive communication (Dense Urban-IC)
19 | Resilience | N/A | TBD | Qualitative TPR | ITU-R WP5D expected to agree to define a qualitative TPR.
20 | Coverage | N/A | TBD | Not a TPR | It is preferred to use the link budget template similar to IMT-2020 submission.
21 | Security | N/A | Not a TPR | Fine with RAN agreement | Related aspects to be described in the submission template.
22 | Interoperability | N/A | Not a TPR | Fine with RAN agreement | Related aspects to be described in the submission template. Defining a TPR still TBD in ITU-R WP5D.
23 | Sustainability | N/A | Not a TPR | Fine with RAN agreement | Covered by energy efficiency.

## Slide 7
Views on Evaluation Configurations
UE power class
  It is proposed to add 26 dBm for TDD
Number of BS/UE antenna elements
Parameters | Values
Number of BS antenna elements | 700 MHz: Up to 64 Tx/Rx 4 GHz: Up to 256 Tx/Rx 7 GHz: Up to 1024 Tx/Rx 30 GHz: Up to 1536 Tx/Rx
Number of UE antenna elements | 700 MHz / 4 GHz / 7 GHz: Up to 8 Tx/Rx 30 GHz: Up to 128 Tx/Rx

## Slide 8
Thanks!