## Slide 1: Views on 6G ISAC use cases and requirements
3GPP TSG RAN Meeting #109
Beijing, China, September 15-18, 2025
Agenda Item: 8.2.1.4
Source: ZTE Corporation, Turk Telekom, Verizon, China Telecom, China Unicom, Telecom Italia, CAICT, ETRI, Queens University Belfast, Pengcheng Laboratory, Shanghai Jiao Tong University, Sanechips, CATT
RP-252028

## Slide 2
Usage scenarios of IMT-2030
[1] Framework and overall objectives of the future development of IMT for 2030 and beyond, ITU
ISAC is one of the six major usage scenarios for IMT-2030.
ISAC will greatly promote the expansion of application scenarios and assist industry applications in IMT-2030.
Support more completed ISAC functions in 6G, with a greater number of applications becoming a significant trend.

## Slide 3
ISAC use cases in 3GPP
TS22.137 in 3GPP R19 has 32 use cases and can be be divided into three categories.
  Object detection and tracking.
  Environment monitoring
  Motion monitoring
These use cases have covered a multitude of industry and consumer applications. The use cases defined for 5G can be standardized in 6G, while 6G requires even more use cases.
New Use Cases
Better Industrial Applications
Stronger Public Safety
The integration of 6G network-based sensing with non-3GPP sensing methods, such as cameras, radar, and other sensors, will enhance sensing reliability while reducing implementation costs
Smart transportation
Smart Home
Smart City
Smart Factory
UAV
5G Sensing
Greater Social Benefits
6G Sensing

## Slide 4
6G ISAC use case | Ship detection
Ship detection and classification (TR 22.870)
Market Size
Market Segment | Estimated Value / Growth | Timeframe
Maritime Surveillance | USD 35.7 billion | By 2029 [1]
Smart Ports & Shipping | USD 9.8 billion | By 2027 [2]
Motivation
By allowing 6G network to detect and track vessels in real time, ISAC can dramatically improve maritime safety, efficiency, and environmental monitoring. For example, ISAC-enabled networks can support collision avoidance, search and rescue, or the detection of unauthorized vessels even in challenging conditions such as fog or rough seas, the corresponding capabilities are highlighted in the 3GPP TR 22.870 [3].
KPI
[1] Maritime Surveillance Market Size & Share Analysis - Growth Trends & Forecasts (2025 - 2030) Source: https://www.mordorintelligence.com/industry-reports/maritime-surveillance-market
[2] Liu, Fan, et al. "Integrated sensing and communications: Toward dual-functional wireless networks for 6G and beyond." IEEE journal on selected areas in communications 40.6 (2022): 1728-1767.
[3]TR 22.870, Study on 6G Use Cases and Service Requirements, stage 1 (Release 20)
Sensing service category | Accuracy of positioning estimate by sensing (for 90% targets) |  | Accuracy of velocity estimate by sensing (for 90% targets) |  | Max sensing service latency [ms] | Missed detection [%] | False alarm [%]
 | Horizontal [m] | Vertical[m] | Horizontal [m/s] | Vertical [m/s] |  |  | 
1 | ≤100 | N/A | N/A | N/A | 5000 | 5 | 5
2 | ≤10 | N/A | N/A | N/A | 5000 | 5 | 5

## Slide 5
6G ISAC use case | Infrastructure collapse monitoring
Market Size
Motivation
ISAC has the potential to revolutionize how we respond to sudden infrastructure collapse such as subsidence and landslides, especially in critical environments like highways, farmlands. The rapid detection and precise localization of a disaster event are crucial for saving lives and minimizing property loss.
KPI
Infrastructure collapse monitoring (TR 22.870)
Market Segment | Estimated Value / Growth | Timeframe
Disaster Management | USD 222.2 billion | By 2027 [1]
Smart Sensing for Geological Hazards | Multi-billion USD | By early 2030s [2]
[1] Liu, Fan, et al. "Integrated sensing and communications: Toward dual-functional wireless networks for 6G and beyond." IEEE journal on selected areas in communications 40.6 (2022): 1728-1767.
[2] Disaster Recovery as a Service (DRaaS) Market by Service Type (Backup & Restore, Real-Time Replication, Data Protection), Deployment Mode (Public Cloud, Private Cloud), Organization Size, Vertical and Region - Global Forecast to 2028, https://www.marketsandmarkets.com/Market-Reports/recovery-as-a-service-market-962.html
Accuracy of positioning estimate by sensing (for 90% targets) |  | Accuracy of velocity estimate by sensing (for 90% targets) |  | Max sensing service latency [ms] | Missed detection [%] | False alarm[%]
Horizontal [m] | Vertical [m] | Horizontal [m/s] | Vertical [m/s] |  |  | 
4 | N/A | N/A | N/A | 100 | 1~2 | 1~2
Deployment scenario support for both Highway & Rural (RMa) (TR 38.913)

## Slide 6
6G ISAC use case | Structural health monitoring
Market Size
Motivation
As urbanization accelerates and infrastructure ages, monitoring the subtle movements of critical structures, such as bridges, flyovers, and skyscrapers has become increasingly important for public safety and asset management. These structures are constantly exposed to environmental factors like temperature changes, wind, rain, and even minor seismic activity, all of which can cause deformations or displacements, indicating early signs of fatigue, stress, or potential failure, making their detection crucial for preventive maintenance and extending infrastructure lifespan.
KPI
Structural health monitoring on a bridge (TR 22.870)
[1] Structural Health Monitoring Market Size, https://www.marketsandmarkets.com/ResearchInsight/structural-health-monitoring-market-size.asp
[2] Qin, Yuxiao, Daniele Perissin, and Ling Lei. "The design and experiments on corner reflectors for urban ground deformation monitoring in Hong Kong." International Journal of Antennas and Propagation 2013.1 (2013): 191685.
Market Segment | Estimated Value / Growth | Timeframe
Structural Health Monitoring (SHM) | Was USD 2.5 billion | In 2024 [1]
 | USD 4.1 billion | By 2029 [1]
Accuracy of positioning estimate by sensing (for 90% targets) |  | Accuracy of velocity estimate by sensing (for 90% targets) |  | Max sensing service latency [ms] | Missed detection [%] | False alarm[%]
Horizontal [m] | Vertical [m] | Horizontal [m/s] | Vertical [m/s] |  |  | 
0.1 | 0.1 | N/A | N/A | 5000 | 5 | 5
Carrier phase detection can be considered to monitor the deformation of infrastructure, by continuously monitoring the phase information of the multipath related to the interested building over time. The change of phase would tell the delicate distance change between building and sensing device .
To meet strict positioning requirement, in certain cases a corner reflector could be deployed on the critical position of infrastructure to enhance the reflected beam, thereby improving sensing capabilities [2].

## Slide 7
Proposal
For 6G ISAC, in addition to 5G-A use cases (UAV, Pedestrian, Vehicle, AGV) the following promising new use cases and the corresponding scenarios should be included in TR38.914 for their strong industrial and public safety benefits:
  Ship detection
  Infrastructure collapse monitoring
  Structural health monitoring

## Slide 8
Text Proposal for TR 38.914
5.4.x Sensing services
The 6GR should enable, and improve if suitable, state-of-art sensing techniques, such as RAN-embedded (based on RAN wireless sensing signal) and RAN-external (e.g. Radar, Lidar, Camara, IEEE802.11 station, UWB, etc.).
The 6GR sensing shall exploit high bandwidth, massive antenna systems, network architecture/ functionalities. 6GR sensing shall support indoors and outdoors scenarios.
6GR shall support regulatory sensing requirements.
6GR shall at least support sensing use cases include the detection and tracking of UAV, Pedestrian, Vehicle, AGV and Ship, infrastructure collapse monitoring, and structural health monitoring.
6GR design targets for sensing requirement include:
1. Support accuracy and latency as defined in TS22.137, and TR 22.870 for some use cases
3. Reduced network complexity
3. Reduced device cost
4. Reduced device power consumption
5. Efficient signalling over the air interface and in the network
6. Support for hybrid sensing methods
7. Scalability (support for large number of sensing objects)
8. High security
9. High availability

## Slide 9: Thanks