## Slide 1: AMPR alignment between FDD PC2 and PC3

## Slide 2: 1T and 2T comparison (PC2 vs PC3)
One AMPR table apply for both PC2 1T and 2T.
The total power back off (OBOtotal(1T) and OBOtotal(2T) ) shall not be higher than 3dB for PC2 than PC3.
  OBOtotal(1T) = max (MPRPC2(1T), A-MPRPC2(1Tx)) – max (MPRPC3(1T), A-MPRPC3(1T))
  OBOtotal(2T) = max (MPRPC2(2T), A-MPRPC2(2Tx)) – max (MPRPC3(1T), A-MPRPC3(1T))
[0.7dB] is applied for all modulation orders for 2T AMPR comparing to 1T AMPR to account for the RIMD impact if the OBOtotal(2T) is no larger than 3dB, otherwise, OBOtotal(2T) = 3dB is applied.

## Slide 3: 1T and 2T comparison (PCx vs PCy)
One AMPR table apply for both PCx 1T and PCx 2T.
The total power back off (OBOtotal(1T) and OBOtotal(2T) ) shall not be higher than AdB for PCx than PCy.
  AdB is the MOP difference between PCx and PCy
  OBOtotal(1T) = max (MPRPCx(1T), A-MPRPCx(1Tx)) – max (MPRPCy(1T), A-MPRPCy(1T))
  OBOtotal(2T) = max (MPRPCx(2T), A-MPRPCx(2Tx)) – max (MPRPCy(2T), A-MPRPCy(2T))
[0.7dB] is applied for all modulation orders for 2T AMPR comparing to 1T AMPR to account for the RIMD impact if the OBOtotal(2T) is no larger than AdB, otherwise, OBOtotal(2T) = AdB is applied.

## Slide 4: AMPR regions between PC3 and PC2
In future, when providing AMPR triangles, the MPR shall be subtracted from the results to align the pure AMPR region.
Companies shall provide the delta total backoff (OBOtotal ) between PC2 and PC3 to facilitate cross check