## Slide 1: Accuracy of EC estimation
Huawei SA2

## Slide 2: Accuracy for Physical Node
Parameters | Meaning
Tr | record period
P(t) | physical expression of instant power
E(Tr) | power consumption
P(Tr) | mean power over Tr
u(t) and i(t) | The u(t) and i(t) are instant values of voltage and current at the AC or DC
The ETSI TS 202 336-12 defines that the measurement of active power and the energy metering shall have the following accuracy:
Accuracy 1 ±3 % from [25 % to 100 % of maximum load] of the equipment (load range 1)
Accuracy 2 ±5 % between [5 % and 25 % of maximum load] of equipment (load range 2)
Energy Consumption is the accumulate value in the measurement interval, therefore different behaviour of variation in EC in the time may lead to the same accumulated resulting value.
Accuracy of estimation of EC at granularity different from Node level cannot be better than the accuracy of the EC at node level.

## Slide 3: Accuracy for Virtual Network function
Accuracy of EC per NF which is a virtual process provided by OAM is higher that those of the EC at physical node.
Sum of the EC consumption estimated for the VNF ECVNF,Estimated , which composes the virtual function
Parameters | Meaning
VCpuUsageMean | mean vCPU usage
VMemoryUsageMean | mean memory usage
VDiskUsageMean | mean disk usage
IOTrafficVolume | sum of the incoming and outgoing traffic volumes
Measurement uncertainty:
EC of the Physical(s) node; -- previous page
Estimation of resources used by the virtual function. This number has not associated a minimum accuracy to be satisfied.
Estimation of resource is the performed considering the mean value on the measurement interval.

## Slide 4: Accuracy due to data volume measurement
Factor 1: Accuracy of counting the bits at node level and at smaller granularity (e.g., at PDU session);
  For the Node level EC this is outside the SA2 scope, and it may be determined be based on statistic considerations;
  The re-transmission in the air interface is not fully considered in TS 28.552 (Only PDCP SDU Data Volume);
Factor 2: Variation along the measurement interval due to time variation.
  Related to how the measurement is performed;
  The effect of traffic variation in time due to, i.e. load, are not currently considered in the measurement of the EC at node level;
Factor 1: Accuracy of counting the bits at node level and at smaller granularity (e.g., at PDU session);
Factor 2: Variation along the measurement interval due to time variation.

## Slide 5: Conclusions
Following considerations shall be taken into account for the selection of solutions to be considered in normative phase.
  Accuracy of estimation of EC at granularity different from Node level cannot be better than the accuracy of the EC at node level.
  Accuracy of EC per NF which is a virtual process provided by OAM is higher that those of the EC at physical node.
  Accuracy of measurement of DV is due to:
  The accuracy of counting the bits at node level and at smaller granularity (e.g., at PDU session), for example the packet lost and retransmission is be not considered properly
  The effect of traffic variation in time due to, i.e. load, are not currently considered in the measurement of the EC at node level;
  And the following shall be considered as well:
  Accuracy of the EC measurement at node level is not under the remit of SA2.
  The time variation in the measurement interval of EC at NF and DV depends by several factors which difficult to take into account.
    as thumb rules smaller is the measurement interval, e.g., 5 minutes, less that variation can be more precisely detected, but the system needs to dedicate more resources increasing the load and energy consumed. Considering the measurement interval can be in range from 5 Minutes to several hours/days the operator and the AF may decide which is the suitable interval for the scope.
It is proposed to reflect those aspects in Clause 7, Agreed Principles for KI#1