## Slide 1: Discussion on management enhancements related to NR MIMO
Source: China Unicom

## Slide 2
Background
With the rapid emergence of new services such as UAV, NTN and major activities assurance scenarios , an efficient and flexible NR MIMO management mechanism is essential to support 3-D coverage optimization and frequent modifcation.
NTN scenario：Satellites move rapidly and beam switching is more frequent.The ground base station beam in fixed, when the beam coverage area changes, it can cause multiple UEs within the beam coverage area to simultaneously avoid beam switching.
Fig1 UAV scenario
UAV scenario：Change from the 1-beam/7-beam for the ground coverage to a 4+3 beam for both ground coverage and aerial coverage.
Fig3 Major activities assurance scenario
Major activities assurance scenario:A large stadium has multiple areas, and the distribution of users unpredictedly varies when hosting large competitions or concerts within a day.
Fig2 NTN scenario
Notes: ﻿

## Slide 3
Background
As the NR construction increases cost for operators , it is necessary to balance capex and opex. Other than coverage optimization, an efficient and flexible NR MIMO management mechanism is essential to support and improve both radio resource and energy efficiency.
Energy Saving based on throughput requirements
This use case considers throughput as main criteria to define the traffic load. It is desirable to use MDA analytics to get throughput prediction for traffic load at the granular level of geographical coordinate. This information can be then used to reduce the coverage of the beam resulting in energy savings.
Fig4 Illustration of SSB beams covering full cell coverage area
Fig5 Illustration of SSB beams modifying to meet the UE centralized coverage with MDAS recommendation
Radio resource optimization based on per SSB usage
the area where a large outdoor stadium holds some competitions is characterized by a high number of users which is challenging to guarantee enough radio resource in this scenario. It is necessary to consider using MDAS to improve radio resource usage.
From: 3GPP TR 28.886 Use case 3: Radio resource optimization based on per SSB usage
3GPP TR 28.866 Use case 1: Energy Saving based on throughput requirements
Fig6 Illustration of SSB beams covering full cell coverage area. | Fig7 Illustration of reduced number of SSB beams covering only hotspot area.

## Slide 4
Background
Massive MIMO sub-features have been proposed and studied in O-RAN. O-RAN Massive MIMO optimization is specified as follows:
Massive MIMO Grid-of-Beams Beamforming (GoB BF) optimization
Massive MIMO Non-GoB Beamforming (Non-GoB BF) optimization
MIMO optimization via MIMO DL Tx power optimization, MU-MIMO pairing, and MIMO mode selection
Initial access (SS Burst Set) configuration optimization
Massive MIMO optimization is one of the top priority use cases in O-RAN. Massive MIMO optimization is one of the top priority use cases in O-RAN. Several massive MIMO sub-features have been proposed and studied during the massive MIMO pre-normative study, which is documented in the O-RAN.WG1.MMIMO-USE-CASES-TR-v01.00, including the potential data requirements for each of the sub-use cases.
Fig8 Massive MIMO Grid-of-Beams Beamforming (GoB BF) optimization
From: O-RAN.WG2.TS.Use-Case-Requirements Massive MIMO optimization
O-RAN.WG1.MMIMO-USE-CASES-TR

## Slide 5
Detailed proposal
WT-1: Analyze and identify management use cases and requirements related to NR MIMO for different scenarios. This work task includes:
• Identify different management scenarios for NR MIMO:
    - 3-D Coverage optimization to support new scenarios, e.g., UAV, NTN and major activities assurance
    - Beamforming and SSB optimization to support radio resource efficiency
    - Beam power optimization to support energy optimization
• Identify whether and how existing specifications can support these identified scenarios.
WT-2: Investigate potential enhancements of configuration and performance management to support fine-grained, flexible and efficient evaluation and optimization.
WT-3: Coordination with O-RAN Alliance: Investigate whether and how existing use cases, requirements and solutions of Massive MIMO optimization from O-RAN can apply to existing NR MIMO management.
A new SID is proposed: Study on management enhancements related to NR MIMO
Including following wort tasks:

## Slide 6
Conclusion
O-RAN has conducted relevant study on Massive MIMO optimization. While SA5 has already investigated some use cases on beam management, but the flexible and efficient capabilities are still needed for further study.
China Unicom propose to initiate a study item in SA5 to investigate potential use cases, requirements, and solutions to enhance existing NR MIMO-related management. O-RAN has conducted relevant study on Massive MIMO optimization
China Unicom kindly requests the discussion and approval of the accompanying documents S5-260407 to proceed with this initiative.