## Slide 1: Relationship between SEALDD and NRM
Cuili Ge –gecuili@huawei.com
Huawei, Hisilicon

## Slide 2: Outline
Compare of SEALDD and NRM
Similar practice in MCX
Deployment/Co-located vs implementation
Business consideration
Way forward

## Slide 3: Compare of SEALDD and NRM
NRM
SEALDD
Rel-16~
Rel-18~
Rel-20
SEAL_Ph4
SEALDD_Ph3
1. SEALDD and NRM have already evolved in parallel and independently for 2 releases.
2. NRM and SEALDD solve different issue and provide totally different service to VAL.
examples
NRM APIs
SEALDD APIs
NRM is aimed at transforming/aggregating the NB APIs to create the new service APIs.
SEALDD is designed to create E2E pipe to deliver the application traffic.
3. The network northbound service APIs can be used by any AFs, NRM, SEALDD, EES, LMS to create their specific service APIs towards the VAL. NRM SHALL NOT be a “gate” to PCF or other network NB APIs.
UE
3GPP network
NRM
VAL server
UE
SEALDD
server
3GPP network
VAL server
3. Regarding the NRM client – NRM server and SEALDD client and SEALDD server interactions. How they are defined rely on the NRM service API and the SEALDD service API, and should be independent with each other.

## Slide 4: Similar practice in MCX
GC1 RP and GCS AS is defined by SA2 in TS 23.468.
TS 23.379
“The MCPTT server is an instantiation of a GCS AS in accordance with 3GPP TS 23.468 [9].”
7.5.2.2 Reference point MCPTT-1 (between the MCPTT client and the MCPTT server)
7.4.2.3.2 MCPTT server

## Slide 5: Deployment/Co-located vs implementation
NRM
SEALDD
Deployment/Co-located
The two has to follow the standard interface
SEALDD
Instantiation/implementation
“Act as the role of NRM server,” or “represents a specific instantiation of NRM server”
They are the implementation, the interaction are internally and does not has to follow the standard interface.
It is at the function development/implementation phase long before the deployment.
NRM
Deployment/collocated is after the function are developed/implemented.

## Slide 6: Business consideration
Currently no commercial deployment of NRM and SEALDD.
So the vendor can have multiple choice per their business requirement and evolution:
Only provide the transformed/aggregated API without touching the data delivery  NRM only
Only provide the data delivery  SEALDD only
Provide both
Phase-I
Phase-II
Add data delivery
Go with 
NRM
SEALDD
Add transformed/aggregated API
Go with 
SEALDD
NRM

## Slide 7: Way forward
Capture both the deployment and implementation way in the annex of TS 23.433.
For the FS_SEALDD_Ph3, allow solutions based on both options and descriptions listed in P5.