## Slide 1: Revoke floor by authorized user
Magnus Tränk (magnus.trank@ericsson.com)
Ericsson

## Slide 2: New stage-2 requirement
New procedure for floor revoke
Defined in TS 23.379 (S6-232729)
Impact on TS 24.380
Impact on statemachines
Floor participant A
(Authorized user)
Floor control server
Floor participant B
(talker)
1. Floor revoke request
3a. Floor revoked
2. Authorization check
MCPTT user at floor participant B is transmitting voice media to the group
3b. Notification to the user
4b. Notification to the user
Floor participant C
(listener)
4a. Floor idle (or multi-talker floor release)
4a. Floor idle (or multi-talker floor release)
4b. Notification to the user

## Slide 3: Floor participant state transition diagram for basic operation
TS 24.380 clause 6.2.4.1
The Client’s state machine
Floor revoke request is different from Floor Request
Floor revoke only when user is in state "has no permission“

## Slide 4: Floor participant state transition diagram for basic operation
TS 24.380 clause 6.3.4.1
Server state machine per MCPTT group call
Addition of Floor Revoke Request when someone has the floor

## Slide 5: Floor participant state transition diagram for basic operation
TS 24.380 clause 6.3.5.1
Server state machine per user per MCPTT group call
Addition of Floor Revoke Request when someone has the floor

## Slide 6: Limitations
Only allowed when user does not have the permission to talk
No ack of the Floor Revoke Request
Not possible to bind an idle or multi talker release message to specific Floor Revoke Request

## Slide 7: Thank You!