## Slide 1: Discussion on Rx BSF UAI
RAN2#131-bis
R2-2507732

## Slide 2: The 2 options (RAN2 classification)
UAI content | Whether prohibit timer is needed | Whether this option implies some restriction on NW configuration. | RAN4 impact
UE preference to quit FBS operation – Option I | No. It’s like one-time report for UE, and it doesn’t need to report the same preference for multiple times. NW may reconfigure and lower down the RSRP/RSRQ threshold, so that UE can quit. Otherwise, UE can still quit FBS operation after 90 seconds. | No restriction on NW configuration. | Align with RAN4 LS, i.e., “RAN4 will not discuss the UE behaviour after reporting UAI”
UE preference to quit FBS operation and UE preference to keep FBS operation – Option II | Yes. After UE reports preference to quit FBS operation, it may revert the preference, i.e., the preference is changed to keep FBS operation. In this case, prohibit timer is needed. Similar to MultiRx feature, the candidate prohibit timer length can be {s0, s0dot5, s1, s2, s3, s4, s5, s6, s7, s8, s9, s10, s20, s30} | No restriction on NW configuration. | ??

## Slide 3: Proposed way forward
P1.on the content of UAI.
P2.on the prohibit timer.