## Slide 1: Motivation for Fragmented Carrier WI in Rel-20
3GPP TSG RAN WG4 Meeting #116
Bengaluru, India, August 25 - 29, 2025
Agenda Item 12
Source: TELUS, Bell Mobility, Apple, AT&T, MediaTek, T-Mobile USA, Southern Linc, Telstra, Vodafone
R4-2511217

## Slide 2: Study Item status and Work Item proposal
Current Status:
  Study item on Fragmented Carrier has been completed as of June 2025 [1]
  Conclusion of the study item is that
    There are potential benefits when using fewer Rx chains than number of component carriers
    It is feasible under certain conditions for a NR UE to operate one Rx RF chain to receive two DL intra-band non-contiguous carriers.
  While there may be additional REFSENS degradation for FDD bands in some scenarios in comparison with the existing requirement due to one Rx RF chain mode, some mitigation methods have been identified to manage the impact of PCell performance degradation.
Proposed Rel-20 Work Item:
  Initiate a Rel-20 work item, including both FDD and TDD bands
  To manage the impact of PCell performance degradation for FDD bands, consider scenarios where fragmented carriers are SCells

## Slide 3: Examples of fragmented blocks in Canada
PCS (n25) example of fragmented spectrum in Toronto*
BRS (n7) example of fragmented spectrum in Toronto*
AWS1/3/4 (n66) example of fragmented spectrum in Toronto*
*Same colour indicates spectrum access for the same operator; each block is 5 MHz wide

## Slide 4: Examples of fragmented blocks in Australia
*Same colour indicates spectrum access for the same operator; each block is 5 MHz wide

## Slide 5: References
[1] RP-251288: TR 38.755 v1.0.0 on Study on NR FR1 DL fragmented carriers