## Slide 1: Draft Session for AIoT
Interim Agreement for Key Issue 1
SA WG2 Meeting #171 Wuhan
Oct. 13 – 17, 2025

## Slide 2: List of Topics
System Architecture in reference point representation
Protocol Stack
UE reader subscription, authorization and revocation
Radio resource management for UE Reader operation
AIOTF discovery and Selection
UE reader selection
UE reader ID allocation

## Slide 3: System Architecture in reference point representation
Open issue:
  Whether the interface between AIOTF and UDM is required.
    UDM is used by the AIOTF retrieve the serving AMF (S2-2508701, S2-2509062)
  WF proposal:
    Agree the architecture figure (left-hand side)
    Whether the interface between AIOTF and UDM is required, depend on the decision on (1) WF decision of AIOTF discovery and selection (2) whether and how subscription information can be fetched by AIOTF from UDM.

## Slide 4: Protocol Stack
  Messages between the UE Reader and the AIOTF are delivered using RRC between UE and NG-RAN and NGAP between NG-RAN and AMF, and using an SBI interface between AMF and AIOTF.
  No open issue foreseen.
  WF proposal:
  capture the protocol stack into conclusion

## Slide 5: UE reader subscription, authorization and revocation
Subscription aspects:
The UE subscription in the UDM will be extended with UE Reader subscription information, which consists of the following:
  information indicating whether the UE is allowed to operate as a UE Reader.
Open issue: Additional subscription information, e.g. validity information, for the UE Reader is FFS
Options proposed for the open issue:
  Validity information: valid time duration and area that allowed for UE to act as an AIoT Reader. (S2-2508700, S2-2508720)
  Allowing TAC list and Forbidden TAC list; (S2-2508878, this can considered as valid area)
  AF ID information indicating that the UE reader belongs to the designated AF; (S2-2508878)
  This validity information can be further used by the AMF to determine whether UE reader authorization needs to be revoked. (S2-2508700)
  Delete the EN directly: no additional subscription information is required.
  WF proposal:
    WF1: NO additional subscription information is needed (i.e. bullet e), or
    WF2: additional subscription information is needed, i.e. bullet a and bullet c (no other parameter bullet will be considered )
    *** If WF2 is the agreed WF, FFS which NF is used to store the additional subscription information (for future meeting)

## Slide 6: UE reader authorization and revocation
Rel-19 interim conclusions:
UE Reader subscription information is available to AMF .
If AMF receives, as part of the subscription information, the indication that the UE is authorized to operate as a UE Reader, together with the “UE reader capability” signalled from UE to AMF, then AMF informs NG-RAN that the UE is authorized to operate as a UE Reader.
WF proposal 0: Add the cyan texts to complete the bullet of R19 interim conclusion.
If the subscription information has been revoked, the indication that the UE is not authorized to operate as a UE Reader from the UDM, then AMF informs NG-RAN that the UE is not authorized to operate as a UE Reader.
Open issue1: Whether UE Reader subscription information is available is required to be available to AIOTF;
WF proposal 1:
WF 1: AIOTF does not need to have UE reader authorization, or
WF 2: AIOTF can obtain UE reader authorization from AMF, or
WF 3: AIOTF can obtain UE reader authorization from UDM

## Slide 7: UE reader authorization and revocation
Open issue2: Whether AIOTF can trigger the UE reader revocation.
  In S2-2508700: AIOTF may determine UE reader authorization needs to be revoked based on
    Local configuration that is related to the SLA.
    AF request to revoke the specific UE reader (s).
WF proposal:
WF1: support AF triggered UE reader revocation (via AIOTF), or
WF2: not to support AF triggered UE reader revocation
Open issue3：Whether and how to enable authorization to the UE is FFS. Options proposed:
  The UE reader is informed by the AmbientIoT Policy from PCF (S2-2508303)
  The AMF provides authorization information or the revocation information to UE (S2-2508317, S2-2508398, S2-2508700(Optionally), S2-2509062(the AMF assigns a UE Reader ID to the UE), )
  The UE not required to be informed and EN is deleted directly (S2-2508660)
  WF proposal:
  WF1: AMF does not provide authorization information to the UE reader, or
  WF2: AMF provides authorization information and the revocation information to the UE reader

## Slide 8: Radio resource management for UE Reader operation
Radio resource management for UE Reader operation:
If the gNB has received the indication that a UE is authorized to operate as a UE Reader, then the gNB may assign radio resources to the UE for UE Reader operation.
The UE Reader is assumed to request radio resources for Reader operation (e.g. taking into account assistance information received from the AIOTF) from the gNB.
NOTE: The details of UE Reader radio resource management will be defined by RAN WG2.
Open issue 1:Whether to capture the above statement in TR 23.700-30.
  WF proposal:
  Capture the first bullet (green) into conclusion, and
  Not to capture the second bullet (cyan) into conclusion, and
  Reword the note
Open issue 2:Whether to report the following info from gNB to CN.
The gNB reports the amount of the radio resource used for AIoT operations, number of devices is operated, and the time period for AIoT operations for charging
  WF proposal: Not to support the feature

## Slide 9: UE reader selection
Fixed UE reader selection (Coverage controlled by operator)
  Assumption: AIOTF configures the UE Reader configuration information (UE reader ID and AIoT Area ID). AF provides the target area info.
  AIOTF selection is performed in Rel-19.
  AIOTF selects the UE reader similarly as RAN reader: AIOTF selects the UE readers (e.g. candidate or final UE readers) based on the received AIoT service operation request and UE Reader configuration information , and provides the selected UE Reader list or AIoT Area ID list to the NG-RAN.
  NG-RAN performs final reader selection.
Mobile UE reader selection (Handheld UE reader)
  AF provides the UE reader ID(s) to NEF;
  NEF performs the ID mapping (from GPSI to internal UE ID);
  NEF selects the AIOTF. (How the NEF selects AIOTF as discussed in page 9.)
  AIOTF provides the UE reader ID to NG-RAN if UE reader is under the service area of the AIOTF.
  Open Issue: how the AIOTF knows the UE reader is in/out of the serving area. Options:
  Configuring the AMF's TAI list based on the AIOTF's service area boundaries. (S2-2508398);
  The Network keeps track of whether UE Readers are in/out of assigned AIoT service areas (S2-2508951);
  AIOTF determines whether the UE is within the indicated area(e.g., via interaction with AMF/LMF) (S2-2508747);
There cases for UE reader selection:
  Case 1: AF provides area
    Fixed UE reader can be selected, Q is whether mobile UE reader can be selected?
  Case 2: AF provides UE reader ID
    UE reader is determined based on the UE reader ID
  Case 3: AF provides both area and UE reader ID
    Concern to support case 3 from several companies
    WF proposal:
      Case 1: WF1: only fixed UE reader will be supported or WF2: both fixed and mobile UE reader can be selected
      Case 2: UE reader is determined based on the UE reader ID
      Case 3: WF1: support case 3 or WF2: not to support case 3

## Slide 10: AIOTF discovery and Selection, in case AF provides UE reader ID (aka. Case 2 in previous slide )
Open Issue: NRF based or UDM based AIOTF Selection
  NRF based AIOTF selection
    NEF retrieve the serving AMF ID from the UDM->NEF selects the AIOTF Selection using NRF based on the serving AMF (S2-2508879)
  UDM based AIOTF selection (S2-2508660)
    NEF retrieve the serving AIOTF from the UDM;
    The serving AMF registers the serving AIOTF information to the UDM
    If the UDM based AIOTF selection is as WF, then to determine 2 or 3(the serving AIOTF information directly registers its ID to the UDM)
WF proposal:
  WF1: Option a, or
  WF2: Option b1, or
  WF3: Option b2

## Slide 11: UE reader ID allocation
Open issue: whether the UE reader ID allocation is required? If required, which entity will allocate the UE reader ID.
  gNB allocates the UE reader ID (S2-2508398)
  AMF allocates the UE reader ID (S2-2509062)
  AIOTF allocates the UE reader ID (S2-2508660)
  Existing ID (NGAP UE ID) is used. (S2-2508701)
  WF proposal:
  Addressed in the normative work (no TU left in study work)

## Slide 12: Other aspects