## Slide 1: NES Use Case and Policy
October 3, 2025
Source: Rakuten Mobile Inc.

## Slide 2: Background
RAN Energy Saving: 3GPP TS 38.300 (Clause 15.4) defines key RAN energy-saving features, including:
  Cell switch on/off (Intra-system energy saving and Inter-system energy saving)
  Cell DTX/DRX: Discontinuous Transmission/Reception for the cell.
  SSB-less SCell: Secondary Cells without Synchronization Signal Blocks.
  Spatial & Power Domain Adaptation: Dynamic adjustment of transmission.
  OD-SSB – On-demand SSB broadcast
  OD-SIB1 – On-demand SIB1 configuration

## Slide 3: Problem statement
As new NES features are continuously introduced for NG-RAN nodes, there is a risk of fragmented OAM approaches.
This can lead to increased operational complexity and hinder the efficient deployment and optimization of energy-saving strategies.
A unified policy is necessary to streamline the management of current and future NES functionalities.

## Slide 4: Existing policy in NRM
The O&M requirements are defined in clause 15.4.3 of 3GPP TS 38.300 as below.
O&M may also configure:
Policies used by the NG-RAN node for cell switch-off decision
Policies used by peer NG-RAN nodes for requesting the re-activation of an inactive cell
The minimum time an NG-RAN node's cell should remain activated upon reception of a re-activation request from an eNB.
Existing Energy Saving (ES) Policy Framework:
3GPP TS 28.310, Clause 6, specified use of the ES policy for cell activation and deactivation.
The policy outlines thresholds and conditions that govern when an NG-RAN node activates or deactivates cells.
This mechanism is already established within 3GPP OAM specifications.
3GPP TS 28.541 specifies attributes for CESManagementFunction and DESManagementFunction, which are characterized by their policy-oriented nature.

## Slide 5: Gap in 3GPP OAM specifications
Current Limitations:
While cell-level ES is addressed, a consolidated policy framework for all Network Energy Saving (NES) features is currently lacking.
Need for Consolidated NES policy
Autonomous NG-RAN Operation: There is a critical need to extend the existing NRM framework to create a comprehensive NES policy. This policy would be provided to NG-RAN nodes, enabling autonomous operation for various NES features.
Policy-Driven Feature Management: This consolidated policy would guide the NG-RAN node in activating, deactivating, and managing diverse NES features based on its capabilities and the operator's strategic objectives.
Guided Decision-Making: The proposed framework empowers the NG-RAN node to make independent decisions regarding NES features while adhering strictly to the guidance, conditions, and policies provided by the operator.

## Slide 6: NES Policy Provisioning
Objective: Enable MnS Consumers to configure the NES policies to MnS Producers of NF(s) or NG-RAN nodes or NE(s) by utilizing the existing OAM Provisioning framework and NRM like the CESManagementFunction.
Application: These policies may guide NG-RAN nodes in implementing energy-saving features within the NG-RAN.
Triggering Mechanisms: NES policies may be derived from the consumed PM counters specified in 3GPP TS 28.552 and 28.554.
NG-RAN Actions: Based on policy conditions and target configurations, the NG-RAN node may:
  Activate or deactivate cells and associated carriers.
  Adjust Cell DTX/DRX configurations
  Adjust traffic scheduling patterns to reduce radio equipment power consumption
  Dynamically adjust transmission through spatial and power domain adaptation.
  Utilize SSBLess SCell functionality.
Dynamic Configuration: The NG-RAN node will configure specific energy-saving features when the conditions mentioned in the MnS Consumer's policy are met.
Autonomous Decision-Making: The NG-RAN node retains the ability to make autonomous decisions based on guidance from either the MnS Consumer or operator-provided policies.

## Slide 7: NES Policy – Possible solutions
NES Policy NRM Fragment
The establishment of a common NES policy that encompasses all NES features handled by NG-RAN nodes.
This policy would be defined within the existing NR NRM to avoid fragmentation and leverage established interfaces.
Notes: @startuml
skin rose
skinparam ClassStereotypeFontStyle normal
skinparam style strictuml
hide empty members
together {
Class GNBDUFunction <<InformationObjectClass>>
Class NRCellDU <<InformationObjectClass>>
GNBDUFunction “1”*-d-“*” NRCellDU
}
Class ESManagement <<InformationObjectClass>> {
Policy Parameters
}
GNBDUFunction "1"*-d--"*" ESManagement
NRCellDU “*”-r-> “1..* ” ESManagement
@enduml

## Slide 8: NES Policy – Key example characteristics
The policy can comprise attributes that dictate critical parameters for NES feature operation, including:
Thresholds: Conditions under which NES features should be activated or deactivated.
Conditions: Specific network or environmental conditions that trigger or influence NES operations.
Targets: Desired energy saving outcomes or performance levels.
Other Relevant Information: Any additional parameters necessary for NG-RAN nodes to autonomously handle various NES features effectively.
Operator Customization:
The policy framework will empower operators to configure their own NES policies based on specific network deployments, traffic patterns, and operational conditions.
NG-RAN nodes may be able to accept and utilize these operator-defined policies to make autonomous decisions regarding NES features, provided they do not violate overarching network policies.
Service Quality Assurance:
    A fundamental principle of this policy is to ensure that the implementation of NES features does not compromise user service quality.
    The policy attributes and NG-RAN node behavior will be designed to prioritize maintaining agreed-upon service levels.

## Slide 9: Advantages
Utilize 3GPP NR NRM to provide NES related policies:
  Utilize established 3GPP OAM Provisioning framework to configure the policy on RAN Network Function, which can be used by O-RAN Network Energy Savings, streamlining integration and avoiding duplication.
Enable NG-RAN Autonomous NES Decisions:
  Empower the NG-RAN node to autonomously activate/deactivate energy saving features and energy optimization actions within NG-RAN node based on policy guidance.
  NES decisions can account for dynamic user load and scheduling requirements to optimize energy use without impact.
Adapt NES to RAN Nodes:
  NES policies can be aligned with the specific functionalities supported by the NG-RAN node.
Consider UE Requirements for NES Activation:
  NES policy application can consider in UE demands to maintain service requirements and quality.
Dynamic policy generation based on service demand and KPI feedback

## Slide 10: Conclusion (To be endorsed)
Unified NES Policy for NG-RAN: Establish a common NES policy to cover all NES features handled by NG-RAN nodes. This policy will be extensible, allowing for the addition of new attributes as future NES features are defined.
Leverage 3GPP Provisioning MnS Framework: Operators (consumers) may configure this policy using the existing OAM Provisioning framework, ensuring consistency and avoiding fragmentation.
Comprehensive Attribute Definition: The policy will include attributes that specify:
  Thresholds: Activation/deactivation criteria for NES features.
  Conditions: Environmental or network states influencing NES operations.
  Targets: Desired energy saving outcomes.
  Other Relevant Information: Any additional data required by NG-RAN nodes for autonomous NES feature handling.
Support vendor extensions: To define their own NES strategies based on network deployment and conditions. These can be vendor specific attributes.
Standardized generic NES policy IOC and use case specific attributes for relevant 3GPP Rel18 and Rel19 NES use cases