## Slide 1: Comments and concerns related to disabling a user device
Ericsson
Rana.alhalaseh@ericsson.com

## Slide 2: Content
Stage 1 requirements
Missing aspects related to remote disabling
  Limited access capability in TS 33.180
  Limited access capability due to immediate disabling
  Disabling scenarios/ targets
  Mapping of MC UE vs MC client vs MC user

## Slide 3: Stage 1 requirement TS 22.260, cl. 6.13.4 access control
[R-6.13.4-001] The MCX Service shall support suspending or disabling of access from an MCX UE or an MCX User to the MCX Service.
[R-6.13.4-002] An MCX User who has a profile that has been deleted or suspended shall be prevented from using that MCX Service User Profile to access the MCX Service.
[R-6.13.4-003] The MCX Service shall provide a mechanism to temporarily disable an MCX UE remotely by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-004] The MCX Service shall only allow a user to affiliate to or select an enabled MCX Service Group (i.e., not disabled).
[R-6.13.4-005] A temporarily disabled MCX UE, which has limited access capability per Mission Critical Organization policy, shall be able to be re-enabled by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-006] The MCX Service shall provide a mechanism to re-enable a temporarily disabled MCX UE by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-007] The MCX Service shall provide a mechanism to permanently disable an MCX UE by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-008] The permanently disabled MCX UE shall remove all MCX Service User Profiles stored in the MCX UE.
[R-6.13.4-009] The permanently disabled MCX UE shall have no access to MCX Services.
[R-6.13.4-010] The security solution for the MCX Service shall minimize the impact of a compromised MCX UE on other MCX UEs.

## Slide 4
Observations:
  So far we saw proposals to temporary disable/enable an MC UE device
  The solution requires limited access capabilities
  The requirements also include disabling an MC user, e.g., corrupt officer
  The solutions require to be secure with minimum impact on other users
A possible way forward is to disable an MC UE device temporary first, then disable it permanently
The solution may be the base to disable a certain MC user
Disabling an MC UE device or MC user needs to be executed immediately
Stage 1 requirement TS 22.260, cl. 6.13.4 access control

## Slide 5: What does an MC UE device mean?
What does an MC UE device mean?
  MC service UE: A UE that can be used to participate in one or more MC services and recording admin and replay services. (ref. clause 3.1 of 23.280)
  MC UE device = MC client(s) hosted/ associated with an MC UE
Question 1: do MC operators need to have the MC UE to be de-attached/de-registered from the 3GPP network?
  Currently we do not have a proper identity mapping between a client (device) vs UE vs user
Disabling scenarios:
  A 3gpp device that hosts an MC client(s)
  A non-3gpp device that hosts an MC client(s)
  An MC user at any of those devices
  An MC gateway UE

## Slide 6: Missing aspects related to remote disabling
There is no aspects specified in 23.280 about limited access and log off from a client
  What is the client behavior to achieve limited access?
  How does log off happen? A client needs to be logged off from all servers
Question 2: how to define limited services based on the MC organization policy?
  [R-6.13.4-005] A temporarily disabled MCX UE, which has limited access capability per Mission Critical Organization policy, shall be able to be re-enabled by the MCX Service Administrator or an authorized MCX User.
  E.g., do MC organizations want to keep track the location of a disabled UE/disabled user, activate ambient listening, etc.?

## Slide 7: Limited access in 33.180, cl. 5.1.1
If an MCX UE completes SIP registration in Step B prior to performing MCX user authentication in Step A and MCX user service authorization as part of Step C, the MCX UE shall be able to enter a 'limited service' state. In this limited state, where the MCX user is not yet authorized with the MCX service, the MCX UE shall be able to use limited MCX services (e.g. an anonymous MCX emergency communication). The MCX Server is informed of the registration of the MC UE with the SIP core though Step B-2.
Figure 5.1.1-1: MCX authentication and authorisation
A way to reach limited services is described above
However, the way to achieve limited services by disabling a UE immediately (not waiting a refresh token) is not clear
informed

## Slide 8: Limited access in 33.180, cl. 5.1.1
Immediate disabling of an MC UE (MC clients) needs to be reflected at these servers
We need to define limited services for MC UE/ MC user who is immediately disabled
  Do MC organizations want to keep some services for disabled MC UE/MC user, e.g., location services, ambient listening?
  If yes, the behavior of the MC client needs to be reflected accordinly.
Figure 5.1.3.1-1: MCX user service authorization

## Slide 9: Limited services vs deployments scenarios
Any security concerns given the defined limited services in 33.180 based on the deployment scenario?

## Slide 10: Thank You!