## Slide 1
Charter Communications’ views on 6G studies in RAN WGs
3GPP 6G Workshop, Incheon, S. Korea
Agenda Item 4
6GWS-250239

## Slide 2: Seamless & Ubiquitous Connectivity
    Support for non-3GPP access types—e.g., Wi-Fi, Wireline and associated capabilities
    Support for low latency traffic (e.g. L4S in RAN and across RAN-Core interfaces)
    Support for high data rates in the UL
    Higher modulation order (1024 QAM) exhibits availability of at least 50% and 35% on UL in RMa and, respectively, UMa (system level simulations)
    Enable selective reduction of reference signals periodicity(ies) to accommodate low mobility use cases (e.g., CPEs)
    6G operation in new band
    7.125 GHz-8.4 GHz

## Slide 3: MIMO Enhancements
    Partially- and fully-coherent codebook for 3TX UEs
    DFT-s-OFDM multi-layer MIMO for UL and DL
    Frequency selective precoding (closed-loop)
    Cooperative MIMO for inter-cell/inter-mTRP interference
    Coherent JT is specified in 5G, with strict requirements on network deployment
    Need more practical interference handling

## Slide 4: AI/ML and Communication
    AI/ML Mobility
      Enhanced RRM measurement procedures to RRM prediction
      Include cell-level prediction and beam level prediction for RACH resource configuration)
      Focus on spatial- and frequency-domain predictions to achieve measurement reduction
      Support RLF prediction and RLF avoidance
      Support beam failure prediction
      SI to study LTM (L1/L2 triggered mobility) and conditional handover
      FR1-FR2 inter-frequency prediction (frequency and spatial domain)
      Inter-RAT mobility handling

## Slide 5: Mobility Enhancements
    LTM enhancements
    Conditional LTM for inter-cell
    Secure L2 signaling
    Early UL sync by sending preamble to target cell in advance
    Inter base station support for RACH-less HO (legacy L3 mobility)

## Slide 6: Network Energy Savings (NES)
    Use on-demand signaling to streamline control and measurement overhead
    On-demand spars(er) SSB, CSI-RS and SIBx information
    Reduced PDCCH monitoring

## Slide 7: Integrated Sensing and Communication (ISAC)
    Support for shared spectrum scenarios whereby, based on country regulations, commercial mobile service users in certain bands may need to share the spectrum with same-band incumbents—while using same or different frequencies, with or without guard bands.

## Slide 8: AI/ML for NG-RAN
    AI/ML for LTM mobility
    Optimized selection of LTM candidate cells
    Optimized trigger for early synchronization and cell switch
    Minimization of LTM reconfiguration/signaling overhead reduction
    AI/ML for Network Energy Savings (NES)
    AI/ML for QoE optimization
    AI/ML-based QoE performance guarantee during mobility
    QoE prediction for resource allocation
    QoE measurements collection for prediction validation.