## Slide 1: T-Mobile’s Vision & Priorities for Next Generation RAN
3GPP 6G Workshop March 2025 Inchon, KR
6GWS-250017

## Slide 2
What Have We Learned from 5G Deployment?
No fundamental RAN network architecture difference between 4G and 5G
One-pipe-for-all RAN is not commercially viable to support all new verticals promised by 5G
Conventional mechanisms (5QI, Slicing) for service quality control is too coarse and static to meet new vertical requirements while maintaining reasonable spectrum efficiency
5GA will NOT be able to address those new verticals effectively.
The faster, the “dumber”.
A needed capability to allocate channel/resources to minimize self interference
The 5G triangle credit: ETSI
FWA
Successful with pain points

## Slide 3
Intent Based Connectivity in 5G Advanced
5GA Tools-in-the Box provide opportunities for intent based Connectivity and Radio Resource Management
5G/5GA Features | Benefits | Limitations | Real time RAN service awareness
Network Slicing | Supported today | Static, provision based. Rely on device OS support. | Limited
QoS (5QI) | Supported today | Static and coarse. Not KPI based | Limited
L4S | RAN level real time adaptation for latency sensitive applications | Limited IP level congestion information | Limited
URLLC | Reduce RAN latency only | Only UL enhancement features available. No ecosystem for mini-slot | No
UE grouping | RAN level RRM based on UE type/group/capabilities | Only works for UEs with specific type of service, e.g. IOT. However, no differentiation within the same UE group. | Limited
However, all those are far from enough for making RAN capable of supporting new verticals that have been promised by the industry

## Slide 4
FWA “Fallow Capacity” Model Works but at a High Price
Chart: $$$
Service differentiation for traffic through the FWA device – Opportunities for value added services
Static/Semi-static radio resource sharing between eMBB and FWA – Lose spectrum efficiency
Flat ARPU
15x eMBB data consumption
Over designed RAN protocol (mobility, link adaptation, RRM) for smartphone applications – lose RRM efficiency and add device complexity
FWA
eMBB
Not needed
Mobility procedures and associated measurement reports/events
UE power saving features
Can be simplified or improved
Channel estimation and MU-MIMO pairing algorithm
Beamforming
IMS voice and emergency service procedures in FWA
Link adaptation
SIB messages
UL MIMO and beamforming
NAS procedures
Today
FWA consumes significant chunk of network resources

## Slide 5
RAN Strategy for 6G
Fundamentals
  Legacy Services: EMBB and voice must be supported on Day 1 in 6G and continue to evolve and enhance the technology into 6G era for spectrum efficiency and better customer experience.
  New Use 6G Cases: Focus on addressing the new use cases or use cases that CANNOT be effectively supported by 5G/5GA.
    The 6G specification should not be limited by the current protocol and RAN architecture.
Start Small and Build Smart – Scalable Architecture
  Start simple with each slice or module focusing on specific use case with specific protocol or architecture that is best suited for the application – Modular 6G architecture approach
  Define architecture/protocol that allow easy addition of new slice or module.
  Drive AI-RAN to set the foundation for Integrated Communication and Computing platform that enables service aware access for different verticals – Programmable RAN

## Slide 6
6G RAN Expectations: Less Revolution, More Evolution
Spectrum
  Clean migration/sharing of existing spectrum from/between 5G to 6G (MRSS).
    Avoid mistakes made in 5G with Dynamic Spectrum Sharing (DSS)
  Re-use 5G Band Combinations and Power Classes for 6G
  Enable new capabilities to leverage the unlicensed spectrum which were not well utilized in 4G/5G
Performance gain
  Performance gain should be service specific, and user experience centric: Service Aware RAN is essential.
    The UE must be able to understand the RAN conditions
  Continued improvement on radio link efficiency
    Important to support existing eMBB centric services and new use cases.
  New or improved air interfaces/protocols: needed to support new verticals, sensing, FWA, etc.
    Should be integral part of the overall 6G RAN architecture which is Service Aware in real time
Operation and Energy Efficiency
  RAN needs to have the capabilities to differentiate, prioritize and predict services for decisions that lead to real time coverage and capacity planning which are critical inputs for energy saving or other operation related functions powered by AI
  Cloud native RAN architecture reduces unnecessary coordination among RAN nodes and expedites the decision-making process for energy saving and real time optimization of the network
  And again, Service Aware for RAN is essential.

## Slide 7
6G Success Demands Evolution & Innovation
Evolution: the legacy services that can be efficiently supported by 5GA
eMBB
Existing IOT services
Voice & Message
Regulatory services (WEA, E911, LI etc)
NTN Integration
Revolution: New services, or services that can NOT be efficiently supported by 5GA
Dedicated and Optimized FWA
LPWA/IIOT/Ambient IOT for 6G
Integrated Sensing and Communications (ISAC)
Cloud & AI native platform: Enabler for multiple stacks/protocols for different verticals

## Slide 8
AI-RAN and Integrated Communication and Computing for 6G
RAN Functions
Air interface, Link adaptation, RRM, mobility management
Computing resource management
Realtime orchestration, Energy saving, cross domain coordination/pooling
New RAN capabilities
Edge computing, Programmable for APP developers, AI data collection, model training
GPU/NPU/CPU
Cloud Native
AI Native
AI-for-RAN
AI-on-RAN
AI-and-RAN

## Slide 9
Summary
Evolution of 5G to 6G is critical for legacy services that have successfully been supported by 5G (eMBB, Voice etc)
Fixed Wireless Access 5G service has been highly successful in creating new revenue and market opportunities but it requires significant enhancements and optimizations to make it a long-term 6G success story
RAN service awareness for 6G will improve customer experience, resource utilization, and create new market opportunities.

## Slide 10: THANK YOU
QUESTIONS?