## Slide 1: Enhancements for the 6G System Architecture 2/14/25
tdoc#: 6GWS-250044
Agenda Item: 5
Vision & priorities for next generation system architecture, core networks and protocols
3GPP workshop on 6G
Incheon, Korea, March 10-11, 2025
NSC
NSC Email Contact: nishith.tripathi@nationalspectrumconsortium.org

## Slide 2: System Architecture Enhancements for 6G
Flexible and Relaxed QoS (FRQ)
Hybrid Device and Network (HDN)

## Slide 3: Motivation for Flexible and Relaxed QoS (FRQ)
To accommodate long propagation delays in a GEO-based NTN, the 3GPP introduced a new 5QI (5G QoS Indicator).
The 3GPP has defined QoS for a TN, and additional QoS classes are introduced as needed to accommodate different networks and services.
One type of network (e.g., an NTN) may not be able to meet match the performance of a TN for many different services. At the other extreme, one type of network (e.g., a local area wireless network with edge computing) may be able to perform better than a typical macrocellular or microcellular TN with a centralized core network.
To support many types of services in diverse networks, an operator may want to offer services with more relaxed or more stringent QoS requirements for a network that has different capabilities compared to a typical macrocellular or microcellular TN with a centralized core network. For example, low-resolution videos or reduced-quality voice calls could be offered by an NTN.

## Slide 4: Flexible and Relaxed QoS (FRQ): An NTN Example
Goal: Provide adequate flexibility to service providers to offer diverse services without increasing the number of 5QIs.
Use the existing 5QIs as a baseline.
Introduce scaling factors for key parameters of a given 5QI such as the error rate and the packet delay.
NTN QoS Parameter Value= X* TN QoS Parameter Value.
Generalized Form: Special Network QoS Parameter Value= X* TN QoS Parameter Value.
Example: NTN PLER = X* PLER, where PLER is the normal PLER Packet Loss Error Rate. The TN PLER may be 1% but the relaxed QoS for the NTN is 2%.
Define a suitable range of scaling factors (e.g., X in the example above) that can be used by a service provider to meet the target QoS for their planned services.

## Slide 5: Motivation for Hybrid Device and Network (HDN)
For the radio interface there are two distinct entities: the User Equipment (UE) and the Base Station (e.g., LTE eNB or 5G gNB). A Base Station can be disaggregated into multiple components.
Aerial Network. To provide on-demand or ad-hoc coverage in disaster scenarios such as floods and wildfires or fire in a building, UAVs can be deployed. However, in a typical scenario, the 3GPP supports a UAV UE, which limits the achievable spectral efficiency and throughput due to unscheduled resource utilization and limited UE power. Placing a gNB or a gNB-DU (or a Radio Unit portion of a gNB-DU) on a UAV would be increase the weight, cost, and/or complexity of UAVs.
A higher power UE with scheduling capability (which is a typical Base Station function) can provide enhanced coverage while keeping the weight, cost, and complexity of the UAV low.

## Slide 6: Hybrid Device and Network (HDN): Example Applications
Goal: Combine characteristics of a UE and a Base Station (even selected core network function such as the UPF)
HDN: Higher transmit power, scheduling function
HDN
Enhanced Link Budget
Direct Coverage Unavailable
UE
Base Station
V2X UE
HDN
Roadside Unit
(RSU)
V2X UE
V2X UE
UAV Application
V2X Application