## Slide 1
Scope of Mobility Enhancements in Rel-19
Agenda: 9.1.2.1
Source: Samsung
Document for : Discussion and decision
3GPP TSG RAN#102
Edinburgh, Scotland, December 11-15, 2023
RP-232916

## Slide 2
Baseline Objectives from RAN Chair
RAN chair recently shared his summary for RAN Rel-19 Package in RP-232745.
In general, we are supportive on the summary, and observe there are several discussion points, especially the yellow-highlighted parts.

## Slide 3
Discussion Points and Proposals (1/3)
Regarding additional scenario for inter-CU LTM, e.g. when CU is acting SN:
  It should be noted that Rel-18 already supports (intra-CU) LTM in SN for NR-DC (not EN-DC), and this would be sufficient in most cases, considering the coverage of SN.
  From Rel-18 discussion, EN-DC was ruled out due to substantial specification and implementation impact, and perhaps this principle should be kept for Rel-19.
  However, for NR-DC case, it would be worth to extend the scenario to inter-CU case if it does not require too much standardization efforts.
  Since the Rel-19 WI already contains enough scope, and the feature would be useful only in certain scenario, the scenario with NR-DC can be considered with a low priority.
   Proposal 1: Additional scenarios including NR-DC can be part of Rel-19 discussion with a low priority.

## Slide 4
Discussion Points and Proposals (2/3)
Regarding event-triggered L1 measurement reporting for supporting LTM:
  Rel-19 MIMO also has a potential objective for the event-triggered L1 measurement reporting.
  It should be noted that inter-cell MIMO only includes sTRP inter-cell beam management (ICBM) which does NOT involve changing of serving cell i.e., handover.
  For the mobility discussion, RAN2 may need to introduce e.g., a new MAC CE to perform handover
  However, for UE-initiated beam management, CG-PUSCH or PUCCH can be a good candidate and the discussion does not have to mix together for the different purposes.
   Proposal 2: Keep the separate objective for event-triggered L1 measurement reporting for supporting LTM.

## Slide 5
Discussion Points and Proposals (3/3)
Regarding details on conditional mobility:
  It is quite difficult for operator to find a big motivation to replace the existing L3-based mobility (which works so well over the last few decades) with Rel-18/19 LTM, except to cope with the characteristics of high frequency.
  In such high-frequency scenarios, UE-driven handover under network control i.e., L1-based conditional mobility/conditional LTM would strengthen the justification as it can adapt the channel quickly.
  If conditional LTM is introduced, Rel-18 mechanism e.g., UE-based TA (not early TA)/RACH-less operation can also be re-used together to perform handover with low latency.
   Proposal 3: The scope of conditional mobility in Rel-19 should focus on conditional LTM, and the UE-based TA/RACH-less mechanism can also be included under conditional LTM.

## Slide 6
Thank you!