## Slide 1: Views on Rel-19 RAN4 RRM package
Ericsson
RP-240505

## Slide 2: Measurement delay reduction in FR2
Background:
    In FR2, measurement delay for L1 and L3 measurements can be very long:
      UE Rx beam sweeping takes very long e.g. 8 Rx beam sweeps needed before each sample.
    Longer delay causes more scheduling restriction resulting in throughput loss.
    Some Rel-18 UE implementations can receive data from multiple directions e.g. 2 TRPs.
Objective of the Rel-19 work item includes:
  Study and specify enhanced FR2 SSB-based L3 measurement delay requirements, where enhancements are due to:
    multi-Rx chain in the UE by using faster beam sweeping.
  The enhanced measurements requirements above comprise:
    Intra/inter frequency and inter-RAT measurements for NR/CA/DC in all RRC states.

## Slide 4: Relaxed RLM and BFD for RedCap UEs
Background:
    The relaxed beam failure detection (BFD) and radio link monitoring (RLM) is specified for normal UEs but not for Redcap UE
      Time-domain relaxation of RLM evaluation period and BFD evaluation period was introduced for non-RedCap UEs, see figure to the right.
    UE power saving is more critical for Redcap UEs.
      Scenario with low speed/quasi-static may be common for Redcap
    For 2 Rx RedCap, no substantial workload is expected since legacy work could possibly be reused.
    For 1 Rx RedCap, additional work might be needed.
Objective of Rel-19 extension includes:
  Specify relaxed radio link monitoring and beam failure detection requirements for RedCap based on the Rel-17 relaxed RLM/BFD requirements for non-RedCap UE.
Time
....
With relaxation
....
= Measurement occasion
Figure 1: Time-domain relaxation of RLM/BFD evaluation period
No relaxation