## Slide 1
0
Views on Rel-19 ATG enhancement
3GPP TSG RAN Meeting #103 RP-240154 Maastricht, Netherlands, March 18-21, 2024
Agenda Item: 9.1.4.6
Source: CMCC, China Unicom
Document for: Discussion

## Slide 2
As promising solution for aviation internet, ATG network attracts operators and aircraft industry’s interest to provide services for all passengers during the whole journey. In May 2023, Chinese Ministry of Industry and Information Technology release 4.9 GHz trial spectrum to CMCC for ATG technical testing.
In R18, RAN4 start the standardization that only focus on FR1 single carrier scenario. The details are summarized as below:
Define RF requirements for ATG BS and UE
Evaluate co-existence issue for both ATG synchronized and non-synchronized operation with TN scenarios.
  for the synchronized scenario, ACLR and ACS are derived
  for the non-synchronized scenario, isolation distance is derived
Define enhanced RRM requirements, at least including NR-NR cell reselection requirements, timing requirements, measurement requirements in RRC_CONNECTED to support ATG scenario.
Define new PDSCH/PUSCH requirements for ATG propagation condition (AWGN with doppler) are introduced
Background

## Slide 3
During the standardization discussion, following issues are found which needs further enhancement in R19.
Enhance throughput to meet ATG capacity demand
Fully utilize operators’ spectrum especially for the fragment spectrum
Motivation for Rel-19 enhancement

## Slide 4
Motivation to meet large ATG network capacity demand
100MHz is not enough for ATG network especially for very-busy route
According to the analysis in [3], we assume 144 seats per airplane with 80% passengers, of whom 50% use ATG services.
  when assuming ATG network always use 64 QAM modulation scheme, for hexagon area,
    180km cell radius require 30M CBW for non-busy route;
    90km cell radius require 60M CBW for busy-route;
    90km cell radius require 100M CBW for very-busy routes
  however, when assuming ATG nework use 16 QAM or QPSK due to large propagation loss, larger than 100MHz CBW is required especially for very busy-route.
 | Radius of one hexagon area/km |  |  |  | 
 | 60km | 90km | 120km | 150km | 180km
Non-busy routes | 20.2 | 45.4 | 80.8 | 126.2 | 181.7
Busy routes | 93.2 | 209.8 | 373.0 | 582.8 | 839.2
Very busy routes | 149.4 | 336.2 | 597.7 | 933.8 | 1344.7
Capacity demand for each hexagon with different radius/Mbps [3]
[1] R4-2215482, ATG co-existence simulation assumption, CMCC

## Slide 5
Motivation to fully utilize operators’ spectrum especially for the fragment spectrum
Severe ATG gNB-to-Terrestrial Network gNB interference occurs if ATG and TN use the same/adjacent carriers according to previous co-existence simulation results. Using different operation bands for ATG would avoid such interference. Usually operators prefer operation bands with large frequency range for 5G TN network, therefore fragment spectrum of LTE refarming band is one choice for ATG to avoid interference and fully utilize operators’ spectrum
Using single carrier of LTE refarming band can’t meet ATG network capacity demand considering most LTE refarming bands can’t support max 100MHz CBW and operators may only own narrow spectrum bandwidth for these bands
Inter-band CA could help to aggregate operators fragment spectrum to meet ATG capacity demand and avoid interference between TN and ATG network

## Slide 6
Objective – CA and leftover issues
CA to enhance capacity
  Define ATG BS and ATG UE requirements
  Define RRM Core requirements:
  Define Performance requirements
  Including
    FR1 intra-band CA, e.g. n79C, n41C, n78C
    FR1+FR1 inter-band CA, e.g. n3+n39, n34+n39, n1+n78
R18 leftover issues
  FR1 MIMO: In R18, two kinds of ATG UE types have been defined, one with omni-directional antenna and the other with antenna array. For the UE with antenna array, if dual-polarization antenna is used, UL MIMO can be supported. However, corresponding requirements are not specified in Rel-18.
Notes: SDL需要提吗？

## Slide 7
Detailed core part objective
Objective of Core part WI
Specify RF and RRM requirements for ATG to support FR1 MIMO [RAN4]
Specify the general RF requirements for ATG UE and BS to support CA [RAN4]
  focus on FR1+FR1 inter-band and intra-band CA band combinations for up to 2 bands DL with 1 band UL
  including configured output power, MPR, A-MPR, etc if needed
Specify the band-combination specific RF requirements for ATG UE and BS to support CA [RAN4]
  For all listed NR inter-band CA and intra-band CA for up to 2 bands DL with 1 band UL
    intra-band: n79C, n41C, n78C
    inter-band: n3+n39, n34+n39, n1+n78
  Define applicable frequencies, bandwidth and bandwidth sets
  Analysize combinations that have self-desensitization and for the combinations where self-desensitization exists, specify at least ∆TIB, ∆RIB, MSD, testing points
Specify the RRM requirements to support CA [RAN4]
  including Maximum Transmission Timing Difference, Maximum Receive Timing Difference, SCell Activation and Deactivation Delay, Interruption etc if needed
Specify signaling and capability to support CA [RAN2]
Notes: SDL需要提吗？

## Slide 8
Detailed Performance part objective
Objective of Performance part WI
Specify corresponding RRM performance requirements and test cases for ATG UE [RAN4]
Specify corresponding demodulation performance requirements for ATG BS [RAN4]
Specify corresponding demodulation performance and CSI reporting requirements for ATG UE [RAN4]
Specify test procedures for ATG BS conformance testing and conformance requirements [RAN4]
Notes: SDL需要提吗？