## Slide 1: UE RF topics for Rel-19
RP-240257
3GPP TSG RAN Meeting #103
Maastricht, The Netherlands, 18th – 21st March, 2024
Agenda Item 9.1.4.1
Source: Nokia

## Slide 2
General
Given the focus on workload across RAN WGs and in specific RAN4 it would be beneficial to select a priority topic for the UE RF topics. High-power UE support is useful for uplink coverage which is requested by multiple operators; hence it fits as a good candidate for a Rel-19 priority topic.
Priority for Rel-19 UE RF should be enhancing High-Power UEs
Topics to consider:
Enable PC1.5 support for inter-band EN-DC for handheld UE and FWA
  Additional details on the following slide
Enable PC1.5 support for intra-band contiguous CA with UL MIMO with 2Tx for handheld UE
Enable PC1.5 support for two band inter-band CA with 2Tx and 3Tx for handheld UE and FWA
Additional topics to consider:
Given the currently limited number of PC2 LTE bands it can be considered to introduce a basket for PC2 LTE bands as proposed in RP-233183.

## Slide 3
High-Power EN-DC support
Motivation:
  DC specification TS 38.101-3 already supports:
    PC1.5 and PC2 for both intra-band contiguous and non-contiguous EN-DC
    PC2 for inter-band EN-DC
  LTE specification TS 36.101 already supports:
    Single band high-power operation (PC1/PC2)
    PC2 intra-band contiguous CA
  To enable PC1.5 UL EN-DC both LTE band and NR band needs to be PC2, and with that all requirements are already captured within the respective LTE and NR specification as captured in clause 6.2B.2.3 of TS 38.101-3.
  The missing part is the addition of a column in TS 38.101-3 Table 6.2B.1.3-1 allowing the addition of PC1.5 support.
  Adding PC1.5 inter-band EN-DC support requires minimal specification changes
Proposed WI Objectives:
  Introduce support for PC1.5 UL inter-band EN-DC
Ensuring HPUE support should be a Rel-19 focus topic, including PC1.5 for inter-band EN-DC

## Slide 4
MPR reduction and/or Power boosting
Motivation:
In prior discussions two different approaches have been listed as suggestions for an improved UL coverage via MPR reduction and/or Power boosting:
MPR reduction for UL contiguous CA
Power boosting or MPR reduction for PC2/PC3 with ACLR relaxation with BS indication
According to observations, a large margin exists between current MPR requirement values for e.g. contiguous intra-band UL CA and what can be simulated or measured
 Rel-19 offers an opportunity to revisit and improve MPR definitions which can improve UL coverage
The alternative suggestion of Power boosting for PC2/PC3 with ACLR relaxation and BS indication can be carefully investigated only when it can be guaranteed that there is no co-existence problem with the operation of adjacent spectrum blocks.
Proposed WI Objectives:
Review specified MPR values and determine reasonable MPR values for contiguous RB allocations in the light of practical implementation.
  Improved MPR can be enable enhancement with modified MPR signalling
The difference between
simulated MPR and specified MPR
Current MPR definitions can be revisited in Rel-19