## Slide 1
R20 proposals for power enhancement with relaxed UE Tx EVM and advanced BS receiver
Huawei, HiSilicon, CBN, Charter Communications, China Broadnet, China Telecom, China Unicom, CHTTL, CMCC, Deutsche Telekom AG, OPPO, Samsung, SK Telecom, Spark NZ, Spreadtrum, Telefónica, Telia Company, Telus, Türk Telekom, Verizon, vivo, Xiaomi, Bell Mobility, KPN, LG Uplus, KT Corp, Vodafone, Telstra, Telecom Italia, Reliance Jio
3GPP TSG RAN Meeting #109
Beijing, China, September 15-18, 2025
RP-252827
Notes: TELEFONICA S.A.

## Slide 2
Background
  In RAN#108 meeting, the joint contribution of 23 companies named as R20 proposals for power enhancement with relaxed UE Tx EVM and advanced BS receiver was submitted and discussed.
    It is proposed to reduce UE MPR values with the relaxed Tx EVM requirements for higher modulation orders, i.e., 64QAM and 256QAM. The intention is to enhance the transmission power for 64QAM/256QAM and then to improve the uplink spectrum efficiency.
    Uplink performance becomes more and more important for commercialization.
  After online and offline discussions, the way forward on RAN4 R20 package was endorsed in RP-251879 with the following compromised agreement of potential objective for UE Tx EVM relaxation in R20
  In this joint contribution, we would like to further propose the potential objective of power enhancement with relaxed UE Tx EVM and advanced BS receiver for RAN4 R20 package.

## Slide 3
Proposals: Power enhancement with relaxed UE Tx EVM and advanced BS receiver
  Motivation
    For uplink transmission in dense urban area, it is observed that BS schedules more than 50% transmissions with high modulation orders, i.e., 64QAM/256QAM and high output power (>20dBm) according to our field data and system simulation results.
    Around 1dB enhancement of the UE output power for 64QAM/256QAM can improve the uplink UPT by 30% for user population at 50% CDF, and overall can improve the uplink spectrum efficiency.
    Since the transmission power for 64QAM and 256QAM is mainly limited by Tx EVM requirements, the 6dB relaxation of Tx EVM requirements for 64QAM and 256QAM can achieve the goal of 1dB power enhancement for 64QAM and 256QAM according to our analysis.
      UE transmits the signals with higher power than that following the existing Tx EVM requirement, which makes the transmitted signals being composed with more non-linearity components.
      BS estimates the non-linearity via uplink DMRS and compensate the received signals by using advanced receiver.
    Besides, with the relaxed Tx EVM requirements, UE can save around 10% transmission power for a given output power.
  Objectives for 5G-A UE RF
    Study and, if feasible, reduce UE MPR values with the relaxed Tx EVM requirement for 5G NR higher modulation orders, i.e., 64QAM , 256QAM and enable/disable it under network control
      BS demod scope is included.
      The study is performed based on non-AI-based approach at BS receiver as baseline and without RAN1 impact
      Note 1: This work will be started in Q1’26. If the similar scope (The examples include the enhancements enabled by BS advanced receiver and UE Tx signal modifications. It is noted that referring to these examples in this WF should not be deemed as taking these examples as the baseline or starting point in 6G study) is agreed by RAN4 to be studied in 6G, it will be removed from 5G-A package. In this case, it is possible that 6G related conclusion can be applied to 5G.
      Note 2: No RAN1/2 scope is expected
      Note 3: the proper TU can follow the agreement in RP-251879