## Slide 1
3GPP TSG-RAN #61 RP-131330
Porto, PORTUGAL, 3– 6 September 2013
Source: Huawei
Title: Motivation for the WI proposal: UMTS Heterogeneous networks
Document for: Discussion
Agenda Item: 13.1.1

## Slide 2: Motivation for the WI proposal: UMTS Heterogeneous networks
The SI on UMTS Heterogeneous networks is proposed to be completed at RAN#61.
TR25.800 is presented for approval and the conclusions are captured in the following slides.
It is proposed to open a WI in the following areas:
    Co-channel interference management –
      Solutions to mitigate UL/DL imbalance
    Support for Multi-flow and range expansion
    Mobility enhancement
    NAIC (Network Assisted Interference Cancellation)
      More evaluations are needed and studies will be carried out before specification phase
    Combined cell deployment

## Slide 3: HetNet co-channel deployment (1/3)
Heterogeneous networks offer substantial throughput gains for HSPA. The gains increase as the percentage of UE offloaded from Macro cell to LPN increases.
When placing LPNs within the Macro area, throughput increases significantly as the number of LPNs per Macro area and/or LPN transmit power increases
UL/DL imbalance in HetNet creates issues such as HS-DPCCH reliability and uplink interference, limiting the downlink and uplink throughputs. To increase throughput gains, more UEs can be offloaded from Macro nodes to LPNs by applying the cell individual offset (CIO) to bias towards the LPNs during serving cell selection.
Example Performance
  DL: with 4 37dBm LPNs and CIO=3dB, the gains are in the order of 250% and 100% for the average and 5% UE throughput, respectively, with offloading percentage of about 50%.
  UL: when placing 4 37dBm LPNs per Macro area, around 40% of the UEs are offloaded to LPNs and then above 250% average throughput can be achieved.

## Slide 4: HetNet co-channel deployment (2/3)
Reliability of the control information
  DL: based on this study, it was found that some problems may arise when applying CIOs exceeding 6dB for single Rx antenna UEs and exceeding 9dB for dual Rx antenna UEs.
  UL: to ensure HS-DPCCH reliability boosting of HS-DPCCH or changes in power control/SIR can be done in current networks, or a new uplink pilot channel can be added.
Further gains can be achieved
  when the CIO values are adapted based on the cells’ loading (decentralised biasing)
  by minimizing interferences from UEs not in Soft HO towards Macro and LPN base stations originating from the UL/DL imbalance - limiting macro UL UE throughput, applying different values of CIO or receiver sensitivity level in LPN, ICIC or changing the carrier frequency for UEs

## Slide 5: HetNet co-channel deployment (3/3)
E-DCH decoupling solution was considered in order to minimize negative effect of DL/UL mismatch. It assumes that the uplink scheduling grants are controlled by the LPN while the HSDPA data is transmitted by the macro cell. The LPN could either signal the grants directly over the air or by routing the grants via RNC to the macro cell.
Network Assisted Interference Cancellation (NAIC) was studied and potential benefits and techniques have been identified. Further investigations are needed.

## Slide 6: SF-DC and DF-DC deployment
SF-DC operation improves the system performance at medium to low loading, especially for the cell edge users.
  as the CIO increases and the cell edge burst rate becomes smaller, SF-DC can improve the performance in the range of 50% to 70% for the cell edge
DF-DC operation improves the range expansion gain. With 4 LPNs/Macro, compared to DC only operation with range expansion,
  for interference limited scenario, the 5% UE throughput gain increases from around 128% to 180% while keeping the mean and media UE throughput almost the same
  for noise limited scenario, the average UE throughput gain improves from 226% to 301% and the 5% UE throughput gain improves from 67% to 99%

## Slide 7: Combined Cell
SFN mode is primarily used for legacy users. When the propagation delay offsets between different transmitting nodes are not accounted for, there is a gain of up to 30% seen for legacy users in link simulations and gains of around 6-17% in system simulations. However, when practical propagation offsets are considered, the gains are reduced. System level simulation results have shown a loss of around 5.7%, while link level simulation results show that the loss is around 6% for solution I and around 25% for solution II. This loss is observed in the Pedestrian A channel and is smaller for other multipath channels.
Both system level simulations and link level simulations have shown significant throughput gains with spatial reuse mode as compared to the macro only network. Compared to the co-channel deployment, there is an 8 – 11%loss due to the additional pilot overhead in spatial reuse mode.

## Slide 8: Mobility
For mass small cell deployment, any further focus should be on NCL extension
For speed based mobility, further enhancements can be considered
For small cell discovery and identification, any further focus should be on proximity detection (UE based, NW based, UE based NW assisted) and the relaxed inter-frequency measurements for UE in Non DCH state
For combined cell, mobility benefits could be expected, and no RAN2 mobility impact has been identified
For range expansion, further mobility enhancements (e.g., intra-frequency event triggered reporting on the secondary carrier) can be considered