## Slide 1: Motivation for new WI: Enhanced LTE D2D Proximity Services
Ericsson

## Slide 2: Background
Rel-12 RAN WI on Proximity Services opened in March 2014 covering
  D2D discovery for in network
  D2D unicast, multicast and broadcast communication for both in network and out of network coverage
Rel-13 SA2 WI on Enhanced Proximity Services opened in June 2014

## Slide 3: Proposed RAN Work Item
Enhancements for discovery and communication targeting PS use cases as well as new potential use cases for LTE (ITS)
  meet additional Public Safety service requirements by SA1 & SA2
  includes aspects from Rel-12 that were not completed as well as new features for Rel-13
  support radio requirements for V2V safety broadcast communication for ITS (CAM)
Scope of proposed RAN study item
  LTE direct discovery enhancements => for PS and V2V CAM (in and out of coverage) and for commercial discovery (in coverage)
  LTE direct communication enhancements within and outside network coverage => for PS

## Slide 4: Service Continuity and UE-NW Relaying
The EPC can switch a Rel13+ ProSe unicast traffic session between infrastructure path, relay path and direct path
  The “switch” is decided by the eNB/MME based on available measurements, radio and traffic properties
  The NW can authorize/deny relaying to a specific UE
eNB1
UE1
UE2
Switch
eNB2
UE1-UE2 proximity border
Switch
EPC
eNB1
UE2
UE1
Switch
UE1-UE2 proximity border
UE3
EPC

## Slide 5: Communication Optimizations
Main focus on new measurements and procedures for relaying and service continuity support under EPC control
Additional focus on energy optimization for the scheduling procedure and sidelink power control
Postpone sidelink (single link) spectral efficiency improvements and peak rate enhancements
  Sidelink power control increases system capacity even without advanced feedback and link adaptation

## Slide 6: V2V
Cooperative Awareness Messages (CAM) for vehicular driving security are broadcasted using adapted D2D discovery channels and procedures
  CAM messages are typically 300-500 bytes in length and are delivered every 0.1-1s
  Support for occasionally out of coverage vehicles is required (the out of coverage discovery solutions for NSPS can be largely reused)
The eNB controls V2V resources
  Different RRM strategies are possible within the resources allocated by the eNB
LTE
D2D

## Slide 8: Appendix: Radio Requirements for v2v communication
CAM payload 300-500 bytes (including security)
CAM packets generation frequency: 1-10 Hz
End-to-end delay ≤ 100 ms
Coverage: up to 300 m
Vehicular speed (e.g., 120 km/h)
LTE Carrier shared between WAN and V2V with V2V resources under eNB control
  Minimized performance impact on WAN traffic