## Slide 1: Motivation for WI proposal for L1/L2 eMTC and NB-IOT enhancements in LTE
Ericsson
RP-160200
3GPP TSG RAN Meeting #71
Göteborg, Sweden, 7th – 10th March, 2016
Agenda item 10.1.1

## Slide 2: Justification
Rel-13 introduces two classes of low-cost MTC devices with enhanced coverage and low power consumption:
  eMTC devices with a UE bandwidth of 6 PRBs (1.08 MHz)
  NB-IoT devices with a UE bandwidth of 1 PRB (180 kHz)
It is important to ensure that large amounts of MTC devices and MTC traffic can be handled efficiently in the networks.
  It is desired to ensure that useful higher-layer improvements introduced for NB-IoT devices can be exploited also for eMTC devices, and vice versa.
  It is in many cases more efficient to use multicast transmission instead of unicast transmission, e.g. for rollout of firmware or software upgrades.

## Slide 3: Objective
Physical layer improvements for eMTC devices, e.g.
  Sync signal repetition (for quicker sync acquisition and reduced power consumption)
  UL lower order modulation (for improved UL coverage)
  Use of the entire DL subframe (for improved DL capacity and throughput)
  Smaller UL resource allocation than 1 PRB (for improved UL capacity)
  Longer TTI than 1 ms (for improved user throughput)
  Reduced soft buffer size (for reduced device cost)
  Larger TBS, HARQ-ACK bundling, more HARQ processes, etc. (for improved peak rate)
Higher layer improvements for eMTC devices and NB-IoT devices
  Congestion and overload control in connected mode (to avoid RACH overload)
  Ensure operator control of usage of low complexity and coverage extension features e.g. based on services/subscription (for efficient spectrum usage)
Low complexity multicast functionality for eMTC devices and NB-IoT devices
  E.g. MBMS transmission based on MBSFN or SC-PtM (for device software upgrades)