## Slide 1: Way forward on msg3
RP-160284
TSG RAN#71
7-10 March 2016, Goteborg, Sweden
Source: ZTE

## Slide 2: Background
At RAN2#93 different views were expressed on the content of msg3 for NB-IoT and specifically on the resume identifier(s) for the Resume message:
  Most companies supported the use of C-RNTI (16 bit) + PCI (9 bit), as a sufficient solution for NB-IoT requirements and allowing to limit the NB-IoT msg3 TB size to 64 bits (also to limit UE power consumption)
  Other companies claimed this is not sufficient/flexible enough (also considering non-NB-IoT applications) and supported a new 40-bit Resume ID, provided by the network to the UE in the Suspend message. This would require a NB-IoT msg3 TB size in the order of 80 bits

## Slide 3: Proposals
In the Suspend message the network provides a new “Resume UE ID” (16 bits)
  Note: This solves the flexibility issue by decoupling the UE identifiers for suspended connections from the C-RNTI values in a cell
In the Resume message the UE provides:
The Resume UE ID previously received by the network and - depending on the size of the UL grant:
  Either the PCI (9 bits) of the cell where the connection was suspended
  (-> 64 bits msg3 TB size)
  Or a 24-bit “Cell ID” of the cell where the connection was suspended
  (-> 80 bits msg3 TB size)
    FFS if the “Cell ID” is provided by the network in the Suspend message of derived by the UE from the existing 28-bit CellIdentity (e.g. using the 24 LSB bits)
  Note: this allows the network to decide whether PCI is sufficient and then use a smaller UL grant / msg3 TB size or to require the “Cell ID” and then accept a larger msg3 TB size
The same general approach is adopted for the non-NB-IoT case
  Note: the consequence of this is that a LTE network requiring the longer “Cell ID” in the Resume message always needs to allocate a bigger UL grant than today for msg3
  Further details (e.g. which TB size to use for larger LTE msg3) are FFS