## Slide 1: On support of larger max TBS for TDD UL for eMTC
Ericsson
RP-160335
3GPP TSG RAN Meeting #71
Göteborg, Sweden, 7th – 10th March, 2016
Agenda item 10.7.5

## Slide 2: Background
Cat-M1 has a maximum TBS of 1000 bits in both DL and UL
It has been proposed to specify a larger max UL TBS (~3000 bits) for Cat-M1 in TDD
  RAN1 contributions R1-161041 and R1-161266
  The intention would be to achieve a higher UL peak rate in DL-heavy TDD configurations
  Surveillance cameras has been mentioned as a use case where this would be beneficial
WI core part for Rel-13 eMTC is supposed to be finalized at RAN#71
  Late, sudden changes may have unforeseen impacts in one or more WGs and delay the WI completion

## Slide 3: PUSCH link performance
Assumptions
  Cat-M1
  EPA 5 Hz channel model
  TBS: {1000, 3240} bits
  Number of repetitions: {1, 2, 4, 8, 16}
  Results are for full-duplex FDD  multiply with 0.4 or 0.2 to obtain results for UL/DL conf. #1 and #2, respectively
Results
  Larger TBS will only improve performance for SNR > 0 dB
  Typically the cell-edge SNR is around -4 dB

## Slide 4: Cell fraction where Cat-M1 UEs benefit from larger UL TBS
Propagation model in TR 36.888 Table 5.2.1.3
  L = I + 37.6 log10(R)
  R in kilometers
  I = 130.5 for 2.6 GHz, I = 120.9 for 900 MHz
L3240 - L1000 = 4 dB  (R3240)2 / (R1000)2 = 61% of the normal cell area
  Only users in a smaller part of the cell (61%) would benefit from the larger max TBS
Cat-1 may be more fitting if it is desired to cover the normal LTE cell coverage with somewhat higher data rates
  Cat-1 can use a larger channel bandwidth than Cat-M1 which means that Cat-1 can achieve higher data rates without relying on 16QAM transmission
  And for lower data rates both Cat-1 and Cat-M1 are able to provide enhanced coverage using Rel-13 CE modes A and B

## Slide 5: Conclusions
Only Cat-M1 users in a small part of the cell (~60% of the normal cell area) are expected to benefit from a larger max UL TBS than 1000 bits
  This means that the application cannot rely on these higher data rates being available
Cat-1 may be more fitting if it is desired to cover the normal LTE cell coverage with somewhat higher data rates
  Cat-1 UEs are expected to become available at attractive price levels in the near future
Late, sudden changes may have unforeseen impacts in one or more WGs and delay the Rel-13 eMTC WI completion
Improved data rate (through various means) can be considered in Rel-14
  See separate WI proposal in RP-160200 and RP-160201
Do not further consider increased max UL TBS for Rel-13 Cat-M1