## Slide 1: RP-160412 Agenda: 10.2.2
Additional Requirements for V2V Operation

## Slide 2: Introduction
V2V using D2D WI ongoing – targeting Q3 2016 completion
802.11p/DSRC is the competitive technology -- designed around 15 years ago
LTE V2V can provide better performance due to synchronization, FDM & coding etc.
Regional regulatory and/or use case requirements may make LTE-V2V less competitive
  LTE V2V & DSRC may coexist on adjacent channels in one or more areas
  Maximum PSD limitation may disadvantage LTE V2V compared to DSRC in EU
  Current assumption on maximum relative speed of 280kmph may not be adequate for some regions (EU)
LTE V2V WI should consider regional regulatory/use case requirements
  RAN needs to decide whether to provide area specific, i.e., fragmented & potentially incompatible solutions
  Incompatible solutions ok – vehicles don’t cross areas, auto industry norm, e.g. Left vs. Right hand drive
Current V2V work may lead to sub-optimal design at least for some areas

## Slide 3: Disconnect between current LTE-V2V work & ETSI regulation
Maximum PSD requirement of 23dBm/MHz in some ITS channels
  For LTE-V2V with SC-FDMA UL waveform, this will limit Tx power for narrow-band transmissions
  Disadvantaged compared to DSRC/802.11p due to 10dB lower Tx power
3GPP needs to consider whether a separate design for Europe is needed or not
  Example multi-cluster SC-FDM can be used: up to 10dB higher Tx power
  Con: More susceptible to channel estimation, frequency offset (1200Hz), in-band emissions
  If current design is changed then impact on completion time line
PSD regulations for ITS spectrum may disadvantage LTE-V2V compared to DSRC/802.11p

## Slide 4: LTE-V2V and DSRC/802.11p adjacent channel co-existence
3GPP needs to demonstrate that LTE-V2V can harmoniously coexist with DSRC
  Especially true if DSRC/802.11p is deployed prior to LTE-V2V, then it risks LTE-V2V co-existence within the unlicensed ITS spectrum and/or inhibits technology migration
ETSI ACLR requirements are tighter than current LTE requirements => ~38dBc
Adjacent channel interference from LTE V2V may impact DSRC performance
  DSRC LBT operation
  Increased interference at receiver
Consider adjacent channel coexistence with 802.11p/DSRC as part of the current WI
DSRC/802.11p & LTE V2V can coexist on adjacent channels in multiple areas

## Slide 5: Maximum relative speed assumption for LTE V2V
Current SA1 requirements are for LTE V2V operation with up to 280kmph relative speeds
  Signal design in RAN1 is based on this requirement
Higher speeds maybe required for some regions
  Example: Autobahn in Germany without speed limits
Feedback from operators and auto industry indicates that relative speed of 500kmph is desirable
RAN1 needs to evaluate if current signal design works at 500kmph relative speeds
  If not, then a solution to address the use case is needed
Relative vehicular speeds up to 280kmph may not be adequate

## Slide 6: Proposals for sidelink based V2V WI
Add a new objective 10 for coexistence with DSRC/802.11p
  10) To specify a solution/requirement (if needed) for coexistence of PC5-based V2V operation and DSRC/IEEE 802.11p on adjacent carrier frequencies within the 5.9GHz ITS spectrum [RAN4]
Send LS to RAN1 asking it to investigate relative speeds up to 500 km/hr
Send LS to RAN1 asking it to consider the PSD limitations in its work
Update WID and send LS to RAN1