## Slide 1: Way forward on remaining open issues in TR38.913
3GPP TSG RAN Meeting #73 RP-161599
New Orleans, September 19 - 22, 2016
Document for discussion/approval
NTT DOCOMO, CMCC

## Slide 2: Motivation
The email discussions kicked-off after RAN#71 resolved the majority of the open issues in 38.913.
However, there are still a few remaining open issues to be addressed.
This contribution provides a way forward on the remaining open issues in 38.913

## Slide 3: (1) 7.17 Connection density
Open issue:
QoS definition is missing for this KPI.
Proposed action:
- Add the following QoS definition if there is not proposal on the definition at RAN#73. Keep updating it if the definition is further clarified in RAN1:
“Connection density refers to total number of devices fulfilling a target QoS per unit area (per km2), where the target QoS is to ensure a system packet drop rate less than 1% under given packet arrival rate l and packet size S. Packet drop rate = (Number of packet in outage) / (number of generated packets), where a packet is in outage if this packet failed to be successfully received by destination receiver beyond packet dropping timer

## Slide 4: (2) Mapping between deployment scenarios and usage scenarios for each KPI
Open issue:
The most of tables on mapping between deployment scenarios and usage scenarios for each KPI are empty in Chapter 7.
Proposed action:
Remove empty tables and only leaves tables with numbers.
Strike through empty cells for tables with numbers for only a subset of deployment scenarios or usage scenarios.

## Slide 5: (3) Evaluation methodologies for TR38.913 KPIs
Open issue:
The evaluation methodology for each KPI is not clarified in the TR.
Proposed action:
Discuss and agree on the contents of the table on the next slide.
Add the table on next slide or add new sentences in each part of Section 7 based on the agreed contents of the table.

## Slide 6
Section | KPI | System level evaluation and relevant deployment scenarios (NOTE)
7.1 | Peak data rate | N/A [Analytical evaluation]
7.2 | Peak spectral efficiency | N/A [Analytical evaluation]
7.3 | Bandwidth | N/A [Inspection]
7.4 | Control plane latency | N/A [Analytical evaluation]
7.5 | Use plane latency | N/A [Analytical evaluation]
7.6 | Latency for infrequent small packets | Analytical evaluation and system level evaluation if needed
7.7 | Mobility interruption time | N/A [Analytical evaluation]
7.8 | Inter-system mobility | N/A [Inspection]
7.9 | Reliability | Link level evaluation and system level simulation Indoor Hotspot, Urban Macro, Highway, and Urban grid for connected car
7.10 | Coverage | N/A [Link budget / link level analysis]
7.10.1 | Extreme coverage | N/A [Link budget / link level analysis]
7.11 | UE battery life | N/A [Analytical evaluation ]
7.12 | UE energy efficiency | N/A [Quantitative evaluation]
7.13 | Cell/TRP spectral efficiency | A joint system level evaluation Indoor Hotspot, Dense Urban, Rural, Urban Macro
7.14 | Area traffic capacity | 
7.15 | User experienced data rate | 
7.16 | 5th percentile user spectrum efficiency | 
7.17 | Connection density | Analytical, link level evaluation and system level evaluation Urban coverage for massive connection (Urban environment
7.18 | Mobility | N/A [Link level evaluation with deployment scenario specific operating point ]
7.19 | Network energy efficiency | Inspection as baseline and system level evaluation if necessary For inspection: NA For system level evaluation: at least in 2 deployment scenarios: one coverage limited environment (ex: Rural) AND one capacity limited environment (ex: Dense Urban)
7.20 Evaluation methodology
This section describes the evaluation methodology and relevant deployment scenario
of each KPI in the TR. This is summarized in Table 7.20.1.
Table 7.20-1: Evaluation methodology and relevant deployment scenario for each KPI
  References: RP-160961, RP-160962, RP-160963, RP-160964, RP-160965, RP-160966, RP-160967, RP-160968, RP-160969, RP-160970, RP-160884, RP-160885, RP-160805
NOTE: for evaluations other than system level evaluation, refer to the specific KPI where the evaluation is described
Proposal: The sentence with square bracket in the 3rd column is to be added to each KPI section in the TR and be deleted from this table

## Slide 7: (4) Editorial issue
Do update Table 6.1.2-1 in the TR by removing the square bracket in Table 6.1.2-1 on the number of users per TRP.
This was already resolved in RP-160672 at the RAN#71 meeting.
This is an editorial issue.

## Slide 8: (5) Editor’s notes
Open issue:
There are still some Editor's notes in Section 3.1, 4, 6.1.4, 6.1.8, 6.1.9, 7.3, 7.6, 7.8, 7.9, 7.17, 7.19, 10.1.2.
Definition of terminology TRP in section 3.1
Proposed action:
Propose to solve the issues of Editor's notes by RAN #73.
Email discussions after RAN #72 should be kicked off.