## Slide 1: Requirements of high speed scenario
3GPP TSG-RAN Meeting #73 RP-161688
New Orleans, USA, Sept 19 - 22, 2017
ZTE Corporation

## Slide 2: Motivation - Classic train traffic types [1]
Real-Time Cyclic (RTC) Traffic
  Types: train control information, train rear information, shunting train protecting, etc.
  Reliability in LTE-R: >30s EFP (95% coverage) (Note1)
Real-Time Acyclic (RTA) Traffic
  Types: dispatching communication, dispatching command transfer, transmission of train numbers, train safeguard alarm, DMS, 6C, TCDS, etc.
  Reliability in LTE-R: >20s EFP(95%)
Note1: >30s EFP (95%) means that 95% coverage should fulfill 100% transmission successful rate for more than 30s.
Notes: DMS: Dynamic Monitoring System
6C: 6 checking sub-systems
TCDS: Train Coach Running Diagnosis System
EFP: Error Free Period

## Slide 3: Motivation - Futuristic Railway Mobile Communication
Critical Train Communication [2]:
  Automatic train control communication
  Trackside maintenance warning system communication
  Remote control of engines
  Monitoring and control of critical infrastructure
  On-train safety device to ground communication
  Platform/train interface alert
  Train integrity monitoring data communication
On-train passenger communication
  2016, on-train passenger internet service by China Railway Network

## Slide 4: Motivation – Current Status of Railway Mobile Communication for 5G
Current Objective of European Railway community [2]:
  As GSM-R (Railway) proven as expensive for the railways, both in-terms of capital and operational expenditure, European Railway community has initiated the work to identify a successor for GSM-R, considering the long term life expectancy of ETCS (2050) and the Railway business needs including the critical train services.
Current Objective of 3GPP high speed scenario:
  High speed scenario approved in 3GPP 38.913 mainly concerns about the services used by passengers, and the critical train services are not included.
Notes: ETCS: European Train Control System).

## Slide 5: 5G Requirements - Future Railway Mobile Communication
Mobility
  Support up to 500 km/h or more (including safety margin)
Handover capability
  This capability refers to handover success rate.
System performance
  User experience data rate, 5th SE and so on.
Reliability
  This refers to the high reliable service requirements of Future Railway Mobile Communication System [1]. The reliability needs further clarification.

## Slide 6: Conclusions
High speed train scenario is a significant scenario in 5G.
The requirements of high speed train should be considered in 5G.

## Slide 7: Reference
[1] “GSM-R Interfaces: Class 1 Requirements”, ERTMS/ETCS - Class 1, 10-Oct-2005
[2] “Future Railway Mobile Communication System: User Requirements Specification”, FRMCS Functional Working Group, 29th of March 2016