## Slide 1: Motivation for New Work Item on Enhancements to LTE operation in unlicensed spectrum
Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, Qualcomm
RAN #73, New Orleans, USA, Sept. 19 - 22, 2016
AI 10.1.1
RP-161584

## Slide 2: motivations
Dual connectivity operation with unlicensed spectrum
  Enabler for:
    Scenario with worse backhaul between network layers
Standalone operation in unlicensed spectrum
  Enabler for:
    Neutral host deployments
      Venue specific radio networks

## Slide 3: motivations
Autonomous uplink operation provides huge performance benefits for operation in unlicensed spectrum
Shortened transmission time intervals can improve performance and reduce overhead for operation in unlicensed bands in addition to the known benefits when operating in licensed bands
Group triggering of SRS can improve efficiency and increase performance benefits when operating in unlicensed spectrum

## Slide 4: Objectives
Two phases for RAN1 and RAN2 with first phase completing in Rel-14
Standalone operation of LTE in unlicensed spectrum [RAN1, RAN2, RAN4]
  Support for system information, paging, random access and quick identification of service providers [RAN1, RAN2, RAN4] (Phase 1 for RAN1 and RAN2)
  Support for RRM/RLM/RLF to allow standalone operation [RAN1, RAN2, RAN4] (Phase 1 for RAN1 and RAN2)
  Support for RRM requirements that are suitable for standalone operation (PCell) [RAN4]
  Support for RRC_IDLE [RAN2, RAN4]
  Support for necessary layer 1 control information [RAN1, RAN2, RAN4] (Phase 1 for RAN1 and RAN2)
  Carrier aggregation support between carriers operating only in unlicensed spectrum [RAN4, RAN1, RAN2]
Support dual connectivity with a PSCell and any aggregated SCells operating cells with Frame Structure type 3 [RAN1, RAN2, RAN4]

## Slide 5: Objectives
Study, and specify if needed, support for Autonomous Uplink Access without UL grant based on Instant Uplink solution with necessary modifications [RAN1, RAN2, RAN4]
Specify support for shortened transmission time intervals for DL and UL on PCell, PSCell and SCell with Frame structure type 3, and reduced UE and eNodeB processing times [RAN1, RAN2, RAN4]
Specify necessary enhancements for more efficient triggering of SRS, e.g. group triggering [RAN1] (Phase 1)
The work item should also specify base station and UE core requirements of 5 GHz spectrum to support the above features [RAN4]