## Slide 1
3GPP TSG-RAN #76 RP-170869
West Palm Beach, USA, 5-8 June, 2017
RAN6 Chair: Juergen Hofmann (NOKIA)
RAN6 Secretary: Paolo Usai (ETSI MCC)
Status Report RAN WG6 to TSG-RAN #76

## Slide 2: Meetings
Meetings held since RAN#75 plenary
RAN6 #4 | 15 – 19 May, 2017 | Hangzhou, P.R. China | Huawei
RAN #76 | 5 – 8 June, 2017 | West Palm Beach, USA | NAF3

## Slide 3: RAN6 #4 Statistics (1/3)
Incoming: 72
Total: 170
To be updated

## Slide 4: RAN6 #4 Statistics (2/3)
Rel-13 features: 8
Rel-14 features: 29
Total: 37
for ePOS_GERAN in addition 1 endorsed CR

## Slide 5: RAN6 #4 Statistics (3/3)
Total number of participants attending: 28 (registered for the meeting: 37)

## Slide 6: Executive Summary
In total 37 CRs agreed and 1 CR (to 24.008, under CT1 responsibility) endorsed: eDRX_GSM(2), CIoT_EC_GSM(6), Positioning enhancements(13+1 endorsed), DECOR_GERAN(1), Radio Interface Enhancements for EC-GSM-IoT(12), TEI14 (3).
Liaisons: 0 incoming LS and 1 outgoing LS.
Rel-13: essential corrections agreed for the eDRX_GSM feature.
Rel-13: essential corrections agreed for the CIoT_EC_GSM feature.
Rel-14: Positioning Enhancements for GERAN: Multilateration Timing Advance (MTA) procedure refined to improve interworking with UL data transfer, latency of the procedure and robustness against security threats. Stage 2 refined and all stage 3 CRs for MTA and Multilateration OTD agreed. Performance requirements agreed. WI completed at RAN6#4. WI Summary endorsed.
Rel-14: Dedicated Core Network Support (DECOR_GERAN): 1 essential correction agreed.
Rel-14: Radio Interface Enhancements for EC-GSM-IoT: For CC5, signalling indication for EC TBF and EC-RACH solution consisting of two methods agreed. Stage 2 CR refined and all stage 3 CRs including performance requirements agreed. For Alternative Coverage Class mapping performance requirements agreed. WI completed at RAN6#4. WI Summary endorsed.
Rel-14: Issue raised on Packet Cell Change Notification. CR postponed to RAN6#5.
Rel-14: Work task for eDECOR setup and related stage 3 CRs agreed under TEI14.
List of agreed CRs in RP-170870 which are for block approval at RAN#76.

## Slide 7: General Matters/RAN6 #4 Report Approval
Report of 3GPP TSG RAN WG6 meeting #2, R6-170187 noted.
Report of 3GPP TSG RAN WG6 meeting #3, R6-170188 approved.
Status update provided to delegates on the move of UMTS work from RAN1 / RAN2 to RAN6 becoming effective after RAN#76.

## Slide 8: Liaisons (1/1)
No incoming LSs and 1 outgoing LS.
R6-170299 LS on Release 14 updates of PS LCS Capability and MSRAC (sent to CT1)
  RAN6 informs about the completion of the two Rel-14 features on Positioning enhancements for GERAN and Radio interface enhancements for EC-GSM-IoT and asks CT1 to agree the endorsed draft CR 24.008 in R6-170316 for introducing the corresponding MS capability support.

## Slide 9: Contributions to Rel-13 and Earlier Features

## Slide 10: eDRX_GSM (Rel-13)
Set of 2 correction CRs agreed related to SGSN and BSS handling of eDRX related information for the paging procedure in case of a BVC reset procedure and in case of a BSS not supporting eDRX.
CR 48.018 Removing Unecessary References to eDRX for SGSN Paging Procedure (Rel-13) agreed in R6-170230
  Rel-14 mirror in R6-170231
The agreed CRs are collected in RP-170927 for block approval at RAN#76.

## Slide 11: CIoT_EC_GSM, Core and Perf aspects (Rel-13)
Set of 6 correction CRs agreed related to EC-PACCH mapping for Coverage Class CC1, protection against frequent system information changes due to a malicious BSS and addition of performance requirements for BTS conformance testing:
CR 45.003 Correction of EC-PACCH mapping onto PDCHs (Rel-13) agreed in R6-170232
  Rel-14 mirror in R6-170233
CR 44.018 Protection Against Malicious Changes to System Information (Rel-13) agreed in R6-170236
  Rel-14 mirror in R6-170237
CR 51.021 Add performance requirement values for testing EC-GSM-IoT channels (Rel-13) agreed in R6-170278
  Rel-14 mirror in R6-170279
The agreed CRs are collected in RP-170928 for block approval at RAN#76.

## Slide 12: CS/PS Coordination for Shared GERAN Networks (Rel-13)
WI completed at GERAN#70.
No contributions.

## Slide 13: Contributions to Rel-14 Features

## Slide 14: Positioning Enhancements in GERAN - ePOS_GERAN (Rel-14) (1/4)
Several concept refinements of the Multilateration Timing Advance (MTA) positioning method at RAN6 #4 agreed:
On Further Proceedings for Enhancing Multilateration Positioning Methods, R6-170199 with agreements on:
  Improved interworking of the MTA procedure with pending uplink data transfer (e.g. exception report) to suspend the ongoing MTA procedure.
  Improved latency of the MTA procedure through indication of the last MTA radio access and forwarding to SMLC before MPM timer expiry.
On Security of the MTA method for Position Estimation, R6-170200 and Solving the Security Threat for MTA Positioning Methods, R6-170289 with agreements on:
  Need for improving robustness against security threats for all MTA access methods.
  Inclusion of a set of RANDOM IDs in the RRLP Multilateration Request message, each used per MTA radio access so that integrity of MTA radio access is checked by verifying the RANDOM ID against the set at SMLC.

## Slide 15: Positioning Enhancements in GERAN - ePOS_GERAN (Rel-14) (2/4)
Normative Work
CR 43.059 Multilateration - Miscellaneous correction agreed in R6-170313
  Refinements to functional description of the Multilateration TA and Multilateration OTD procedures (Stage 2).
CR 44.031 Introduction of Multilateration agreed in R6-170323
  RRLP message for the MTA positioning method.
CR 44.031 Introduction of Multilateration OTD agreed in R6-170266
  RRLP message for the MOTD positioning method.
CR 44.018 Introduction of Multilateration, agreed in R6-170294 and
CR 44.060 Introduction of Multilateration, agreed in R6-170296
  (EC-)CCCH channel access and immediate assignment and (EC-)PACCH messages related to paging response and MTA radio access.
CR 48.008 Introduction of Multilateration agreed in R6-170314
  Forwarding of MTA information from non-serving BSS to serving BSS via MSC.
CR 48.018 Introduction of Multilateration agreed in R6-170282
  SGSN and BSS handling of the MTA / MOTD procedure and concurrent data transfer or other location requests.

## Slide 16: Positioning Enhancements in GERAN - ePOS_GERAN (Rel-14) (3/4)
Normative Work (cont’d)
CR 48.018 Introduction of PS domain transport for Multilateration Timing Advance information transfer agreed in R6-170174
  Transfer of MTA related information between a non-serving BSS and a serving BSS in the PS domain using the RIM procedure with modification
CR 49.031 Introduction of Multilateration agreed in R6-170295
  BSSMAP message exchange between BSS and SMLC for the MTA positioning method.
Draft CR 24.008, Introduction of Multilateration and Indication of CC5 support endorsed in R6-170316 and sent along the LS to CT1
  Introduces MS capability indication for MTA and MOTD in PS LCS Capability IE and MS Sync accuracy in MSRAC IE. It also includes the capability bit for CC5.
CR 45.005 Receiver Performance for Extended Access Burst agreed in R6-170270 and CR 51.021 on BTS conformance testing agreed in R6-170284
CR 45.010 Introduction of Multilateration agreed in R6-170297 and CR 51.021 on BTS conformance testing agreed in R6-170317
  Captures timing advance and synchronization accuracy performance requirements for MTA and MOTD methods for MS and BTS.

## Slide 17: Positioning Enhancements in GERAN - ePOS_GERAN (Rel-14) (4/4)
CRs for Approval
The agreed CRs are collected in RP-170923 for block approval at RAN#76.
WI Summary
Summary for WI Positioning Enhancements for GERAN endorsed in
R6-170271, submitted in RP-170920 to RAN#76.
WI Progress
All stage 2 and stage 3 CRs agreed at RAN6#4.
WI completed at RAN6#4.
Status Report to RAN#76: RP-170919
Revised WID for Approval
Revised WID Positioning enhancements for GERAN: RP-171052
  update of impacted specifications and completion time

## Slide 18: Support of Dedicated Core Networks - DECOR_GERAN (Rel-14)
WI closed at RAN#73.
One correction CR agreed at RAN6#4.
CR 48.018 Addition of DECOR rerouting cause code (Rel-14) agreed in R6-170178
The agreed CR is in RP-170926 for approval at RAN#76.

## Slide 19: Radio Interface Enhancements for EC-GSM-IoT (Rel-14) (1/5)
Alternative Mappings for Higher Coverage Classes with 2 PDCHs - Normative work
Core specification completed at RAN6#3.
Performance part completed at RAN6#4.
CR 45.005 Performance requirements for Alternative Mappings for Higher Coverage Classes with 2 PDCHs agreed in R6-170301
  Receiver performance requirements for sensitivity, ACI and CCI for higher coverage classes CC2 to CC5 (CC5 for UL only).

## Slide 20: Radio Interface Enhancements for EC-GSM-IoT (Rel-14) (2/5)
UL MCL Improvement for Low Power Devices in EC-GSM-IoT
Following concept refinements at RAN6#4 agreed:
On indication of CC5 for uplink EC TBF, R6-170250 with agreement:
  Indication of CC5 capability during EC TBF operation using the CPS parameter in RLC/MAC header for higher coverage class used on UL.
Way Forward for CC5 EC-RACH Solution, R6-170293 with agreements:
  Specify Extended Synchronization Access Burst (ESAB) based method and Extended Dual slot Access Burst (EDAB) based method for CC5 EC-RACH.
  Rel-14 MS supporting CC5 is capable of both methods (one capability support bit).
  The network configures the used method for EC-RACH via the broadcast channel and in addition broadcasts CC5 assistance information (signal level range for UL coverage class selection).

## Slide 21: Radio Interface Enhancements for EC-GSM-IoT (Rel-14) (3/5)
UL MCL Improvement for Low Power Devices in EC-GSM-IoT - Normative work
CR 43.064 Introduction of uplink coverage class CC5 for UL MCL improvement agreed in R6-170302 (Stage 2)
  Refinements to functional description to add the agreed EC-RACH solution
CR 44.018 Introduction of new UL coverage class CC5 for UL MCL improvement agreed in R6-170325
  Specifies channel access, channel assignment and broadcast support information.
CR 44.060 Introduction of new UL coverage class CC5 for UL MCL improvement agreed in R6-170308
  Specifies RLC/MAC header adaptation to indicate CC5 and EC-PACCH messages.
CR 48.018 Introduction of new UL coverage class CC5 for UL MCL improvement agreed in R6-170321
  Specifies CC5 as additional uplink coverage class.
Draft CR 24.008 specifying the CC5 capability support, see ePOS_GERAN.
CR 45.001 Introduction of new UL coverage class CC5 for UL MCL improvement agreed in R6-170303
  Adds CC5 logical channels, burst structures and physical channel mapping.

## Slide 22: Radio Interface Enhancements for EC-GSM-IoT (Rel-14) (4/5)
UL MCL Improvement for Low Power Devices in EC-GSM-IoT - Normative work
CR 45.002 Introduction of uplink coverage class CC5 for UL MCL improvement agreed in R6-170304
  CC5 EC-RACH burst structures and physical channel mapping for CC5 channels.
CR 45.003 Introduction of new UL coverage class CC5 for UL MCL improvement agreed in R6-170318
  Channel encoding, burst mapping and physical channel mapping for CC5 channels.
CR 45.004 Introduction of ESAB agreed in R6-170310
  Clarification on non-applicability of blind physical layer transmissions for ESAB.
CR 45.008 Introduction of new UL coverage class CC5 for UL MCL improvement agreed in R6-170319
  MS behaviour for UL CC5 coverage class selection for channel access and related network assistance information.
CR 45.005 Introduction of new UL coverage class CC5 for UL MCL improvement agreed in R6-170322
  Receiver performance requirements for sensitivity, ACI and CCI for CC5 channels.
CR 51.021 Introduction of ESAB agreed in R6-170312
  BTS conformance testing requirements are added.

## Slide 23: Radio Interface Enhancements for EC-GSM-IoT (Rel-14) (5/5)
CRs for Approval
The agreed CRs are collected in RP-170924 for block approval at RAN#76.
WI Summary
WI Summary for WI Radio Interface Enhancements for EC-GSM-IoT endorsed in R6-170326, submitted in RP-171321 to RAN#76.
WI Progress
All stage 2 and stage 3 CRs agreed at RAN6#4.
WI completed at RAN6#4.
Status Report to RAN#76: RP-171320

## Slide 24: Small technical enhancements and improvements (TEI14)
CR 44.060 Handling of PCCN message including a 3G CCN Measurement, R6-170298
  Inconsistency observed for reporting neighbor cells in the Packet Cell Change Notification message in CCN mode for the case that no 3G cells are reported by the MS.
  The corresponding late CR for Rel-14 was postponed to RAN6#5 to allow companies to check the proposed solution.

## Slide 25: Other Rel-14 contributions
Several contributions on eDECOR received.
  The eDECOR feature, providing MS assisted selection of the DCN, involving several 3GPP groups was already completed for (E-)UTRAN for Rel-14 and also GERAN support was included in stage 2 in TS 23.401. However, RAN6 has not been informed to define a stage 3 building block (BB) upon completion of stage 2 work in SA2 (such LS was not received).
  RAN6 decided to define a work task and to complete the normative work under TEI14 at RAN6#4, as a BB could not be completed in Rel-14.
New WI (BB) proposal: Enhancements of Dedicated Core Networks, R6-170179 was thus noted and the set of 3 CRs was agreed for Rel-14:
  CR 48.018 Introduction of enhanced DECOR for GERAN, R6-170263
  CR 44.018 Introduction of enhanced DECOR for GERAN, R6-170265
  CR 44.060 Introduction of enhanced DECOR for GERAN, R6-170291
The agreed CRs are in RP-170925 for block approval at RAN#76.

## Slide 26: Rel-15 related contributions
One contribution New WID on Further Positioning Enhancements for GERAN in R6-170201 was received. This targets
  improved interaction with UL and DL data transfer during the MTA positioning procedure
  enhancements to security of the MTA procedure.
Major aspects of this proposed work were agreed at RAN6#4 to be included in Rel-14 (see ePOS_GERAN discussion), the main remaining aspect being the suspension and resumption of the MTA procedure due to high priority data on DL (network commands), which was considered to have impact to the core network.
The WID proposal was noted in R6-170239.

## Slide 27: Other technical work
Withdrawal of GERAN Iu mode specifications from Rel-12
  The Chairman reported that a request from the 3GPP Specification Manager / ETSI MCC was received to investigate the withdrawal of GERAN Iu mode specifications 3GPP TS 44.118 and TS 44.160 from Rel-12 onwards, as CT have suspended their support of the GERAN Iu mode from Rel-12.
  A need is seen by the 3GPP Specification Manager / ETSI MCC that the 3GPP specifications are kept implementable, which is not the case for GERAN Iu mode from Rel-12.
  Participating companies at RAN6#4 did not raise a general concern on this proposed proceeding.
  More than 100 references in 3GPP specs were identified by ETSI MCC which need to be removed.
  Guidance on the further proceeding is requested from TSG RAN#76.

## Slide 28: Work Plan
Presented in R6-170327 and approved.
Work / Study Item | Objective | Rel (Core Feature) | Completion
WI ePOS_GERAN-Core | Enhanced Positioning in GERAN (Stage 2 + Stage 3) | Rel-14 | 100%
WI ePOS_GERAN-Perf | Enhanced Positioning in GERAN, Radio Performance Requirements | Rel-14 | 100%
WI CIoT_EC_GSM_radio_enh-Core | EC-GSM-IoT Radio Interface Enhancements (Stage 2 + Stage 3) | Rel-14 | 100 %
WI CIoT_EC_GSM_radio_enh-Perf | EC-GSM-IoT Radio Interface Enhancements, Radio Performance Requirements | Rel-14 | 100 %

## Slide 29: RAN WG6 Schedule (2016 – 2018)
Meeting | Date | Location | Host
RAN6#1 | 22 – 26 August 2016 | Gothenburg, Sweden | EF3
RAN#73 | 19 – 22 September 2016 | New Orleans, US | NAF3
RAN6#2 | 14 – 18 November 2016 | Reno, US | NAF3
RAN#74 | 5 – 8 December 2016 | Vienna, Austria | EF3
RAN6#3 | 13 – 17 February 2017 | Athens, Greece | EF3
RAN#75 | 6 – 9 March 2017 | Dubrovnik, Croatia | EF3
RAN6#4 | 15 – 19 May 2017 | Hangzhou, China | Huawei
RAN#76 | 5 – 8 June 2017 | West Palm Beach, US | NAF3
RAN6#5 | 21 – 25 August 2017 | Berlin, Germany | EF3
RAN#77 | 11 – 14 September 2017 | Sapporo, Japan | ARIB, TTC
RAN6#6 | 27 November – 1 December 2017 | Reno, US | NAF3
RAN#78 | 18 – 21 December 2017 | Lisbon, Portugal | EF3
RAN6#7 | 26 February – 2 March 2018 | Athens, Greece | EF3
RAN#79 | 19 - 22 March 2018 | India | 
RAN6#8 | 21 - 25 May 2018 | Korea | 
RAN#80 | 11 - 14 Jun 2018 | North America | NAF3
RAN6#9 | 20 - 24 Aug 2018 | Gothenburg, Sweden | EF3
RAN#81 | 10 - 13 Sep 2018 | Australia | 
RAN6#10 | 12 - 16 Nov 2018 | TBD | 
RAN#82 | 10 - 13 Dec 2018 | Sorrento, Italy | EF3

## Slide 30: Concluding Remarks
A special thanks to Paolo Usai (ETSI MCC) for his efficient secretary support.
Thanks to all delegates for their hard work.
Thanks to the host Huawei for the convenient meeting organization.