## Slide 1: NEW wi on switch of primary carrier for UMTS
RP-171907 - Motivation for New proposed WI

## Slide 2: Background
The current procedure for switching primary carrier is to perform a HS Serving Cell Change which is a rather slow and inefficient.
An enhanced mechanism can make use of pre-configuration through RRC signaling, and the HS-SCCH downlink control channel for instructing the UE to perform the switching of primary carrier in a fastest way via HS-SCCH orders.

## Slide 3: Proposed RAN Work Item
Extend the Rel-12 and 14 fast reconfiguration mechanism Enhanced TTI switch feature for switching the primary carrier in a multi-carrier scenario, so that the primary carrier becomes the secondary carrier and the secondary carrier becomes the primary carrier. Following the Rel-12 and Rel-14 enhancement:
  Information related to the switch of primary carrier may be pre-configured by means of RRC signaling, e.g. when multi-carrier is configured.
  A triggering mechanism by means of a filtered UPH (UE Power Headroom) report in MAC Control Information is defined.
  An execution mechanism by means of an HS-SCCH order is defined.

## Slide 4: benefits
The main advantages of using a simplified HS-SCCH are the following ones:
  Fast mechanism to perform switch of primary carrier
    Avoid a time consuming RRC procedure which may take around 200ms.
    Improved DL control channel and SRB coverage when coverage on high frequency band decreases.
  Small standard impact. Existing work from WI for Multi-carrier enhancements can be reused.